## Slide 1: Infinite Impulse Response Filters

## Slide 2: Outline
IIR biquad filter structures


X
O
O
X
Stability
  Bounded-Input Bounded Output
  Equalization Example
IIR filter design
Conclusion
IIR filter implementation
Filter design demos

## Slide 3: Discrete-Time IIR Filters
Infinite Impulse Response (IIR) filter has impulse response of infinite duration, e.g.
Z
Recursively compute output y[n], n ≥ 0, given y[-1] and x[n]
How to implement the IIR filter by computer?
  Let x[n] be the input signal and y[n] the output signal,
IIR Biquad Filter Structures

## Slide 4: Many Equivalent Representations
Difference equation

x[n]
y[n]
Unit Delay
Unit Delay
1/2
1/8
y[n-1]
y[n-2]
Poles at –0.183 and +0.683
  Recursive computation needs y[-1] and y[-2]
  For the filter to be LTI, y[-1] = 0 and y[-2] = 0
Transfer function
  Assumes LTI system
Block diagram representation
  Second-order filter section (a.k.a. biquad) with 2 poles and 0 non-trivial zeros
IIR Biquad Filter Structures

## Slide 5: IIR Biquad Block Diagrams
Biquad: short for biquadratic
  Transfer function is ratio of two quadratic polynomials

x[n]
Unit Delay
Unit Delay
v[n-1]
v[n-2]
v[n]
b2
a1
a2
b1

y[n]
b0
Express above as cascade of two familiar filters
All-pole IIR Filter
x[n]
v[n]
FIR Filter
y[n]
Two poles, and zero, one or two non-trivial zeros
all-pole section from previous slide
Feedback paths
Feedforward paths
IIR Biquad Filter Structures

## Slide 6: IIR Biquad Transfer Function
Assume LTI system (zero initial conditions)
All-pole IIR Filter
X(z)
V(z)
FIR Filter
Y(z)
H1(z)
H2(z)
  V(z) = H1(z) X(z) and Y(z) = H2(z) V(z)
  Y(z) = H1(z) H2(z) X(z) and hence H(z) = H1(z) H2(z)
Overall transfer function
  Real a1, a2 : poles are conjugate symmetric (  j ) or real
  Real b0, b1, b2 : zeros are conjugate symmetric or real
IIR Biquad Filter Structures

## Slide 7: IIR Biquad Difference Equation
Derive difference equation from transfer function
  Take inverse z-transform of both sides:
  Collect terms to isolate y[n] on the left-hand side:
How to convert biquad to a first-order IIR section?
IIR Biquad Filter Structures
  How many multiplications and additions per output sample?

## Slide 8: First-Order Frequency Response
Pole at p0 = 0.9 and zero at z0 = 0.0
  Angle of pole near unit circle indicates frequency at which peak occurs in magnitude response
  Angle of zero on or near unit circle indicates frequency at which valley occurs in magnitude response
IIR Biquad Filter Structures

## Slide 9: Impact of Zeros on Magnitude Resp.

## Slide 10: IIR Biquad Frequency Responses
Magnitude response
  Zeros z0 & z1 and poles p0 & p1
  |a – b| is distance between complex numbers a and b
  |ej – p0| is distance from point on unit circle ej and pole p0
IIR Biquad Filter Structures

## Slide 11: Frequency Response?
zeroAngle = 15*pi/16;
z0 = exp(j*zeroAngle);
z1 = exp(-j*zeroAngle);
numer = [1 -(z0+z1) z0*z1];
r = 0.9;
poleAngle = pi/16;
p0 = r * exp(j*poleAngle);
p1 = r * exp(-j*poleAngle);
denom = [1 -(p0+p1) p0*p1];
%%% Normalize the DC response
%%% to 1 in linear units by
%%% setting H(z) evaluated
%%% at z = 1 to be 1
C = (denom * [1 1 1]’) / (numer * [1 1 1]');
freqz(C*numer, denom);
Re(z)
Im(z)
X
O
O
X
Re(z)
Im(z)
O
O
X
X
zeroAngle = pi/4;
z0 = exp(j*zeroAngle);
z1 = exp(-j*zeroAngle);
numer = [1 -(z0+z1) z0*z1];
r = 0.9;
poleAngle = pi/4;
p0 = r * exp(j*poleAngle);
p1 = r * exp(-j*poleAngle);
denom = [1 -(p0+p1) p0*p1];
%%% Normalize the DC response
%%% to 1 in linear units by
%%% setting H(z) evaluated
%%% at z = 1 to be 1
C = (denom * [1 1 1]') / (numer * [1 1 1]');
freqz(C*numer, denom);
Re(z)
Im(z)
O
O
X
X
zeroAngle = pi/4;
rz = 1/0.8;
z0 = rz*exp(j*zeroAngle);
z1 = rz*exp(-j*zeroAngle);
numer = [1 -(z0+z1) z0*z1];
r = 1/rz;
poleAngle = pi/4;
p0 = r * exp(j*poleAngle);
p1 = r * exp(-j*poleAngle);
denom = [1 -(p0+p1) p0*p1];
%%% Normalize the DC response
%%% to 1 in linear units by
%%% setting H(z) evaluated
%%% at z = 1 to be 1
C = (denom * [1 1 1]') / (numer * [1 1 1]');
freqz(C*numer, denom);
Lowpass, highpass, bandpass, bandstop, allpass, notch?
Poles have radius r Zeros have radius 1/r
Zeros are on the unit circle
handout

## Slide 12: Demonstrations
DSP First, 2nd ed., ch. 10
  IIR filtering tutorial (Link)
  Connection between the Z and frequency domains (Link)
  Time/frequency/z domain movies for IIR Filters (Link)
link
IIR filter with one pole and a zero at the origin
Movement of Poles
IIR Biquad Filter Structures

## Slide 13: Stability
A discrete-time LTI system is bounded-input bounded-output (BIBO) stable if for any bounded input x[n] such that | x[n] |  B1 < , then the filter response y[n] is also bounded | y[n] |  B2 < 
handout
Proposition: A discrete-time filter with an impulse response of h[n] is BIBO stable if and only if
  Every finite impulse response LTI system (even after implementation) is BIBO stable
  A causal infinite impulse response LTI system is BIBO stable if and only if its poles lie inside the unit circle
Stability

## Slide 14: BIBO Stability
Rule #1: For a causal sequence, poles are inside the unit circle (applies to z-transform functions that are ratios of two polynomials) OR
pole at z=a
Rule #2: Unit circle is in the region of convergence. (In continuous-time, imaginary axis would be in region of convergence of Laplace transform.)
Example:
  Stable if |a| < 1 by rule #1 or equivalently
  Stable if |a| < 1 by rule #2 because |z|>|a| and |a|<1
Stability

## Slide 15: Equalization
Design equalizer to compensate frequency distortion
x[m]
System Model (Filter)
LTI
h[m]
y[m]
Equalizer
LTI
g[m]
  Applications: Audio, image and communication systems
  Goal: Make cascade all-pass:
Example: H(z) is an FIR filter
Re(z)
Im(z)
  Zeros of H(z) become poles of G(z)
  Stability issues?
O
O
O
O
O
X
X
X
X
X
all-pass
notch
notch
cancellation
cancellation
Stability

## Slide 16: IIR Filter Design
Classical IIR filter design algorithms
Design Method | Passband | Stopband
Butterworth | Monotonic | Monotonic
Chebyshev type I | Monotonic | Ripples
Chebyshev type II | Ripples | Monotonic
Elliptic | Ripples | Ripples
Manual placement of poles and zeros
Cascade of Biquads
Automated adaptation of pole and zero locations
  Center frequency of bandpass resonator HW 1.1(d) & 2.1(d)
  Notch filter with parameterized notch frequency HW 3.1(c)

## Slide 17: IIR Filter Implementation
Cascade of biquads for N poles
  N even: N/2 conjugate pairs of poles. Cascade of N/2 biquads.
  N odd: One real pole and (N-1)/2 conjugate pairs of poles. Cascade of first-order filter (real pole) and (N-1)/2 biquads
  For M biquads, M! orderings of conjugate pairs of poles and for each ordering, M! orderings of conjugate pairs of zeros
  Exhaustive search: simulate all combinations to pick best one
  Quick pairing: Order biquads in ascending order of quality factors (see next slide) and for each each biquad, choose the conjugate zero pair that is closest in Euclidean distance
Single section (single difference equation)
  Could make a BIBO stable filter become BIBO unstable
Cascade of Biquads

## Slide 18: Quality Factors for Digital Biquads
For poles at a ± j b = r e ± j , where is pole radius (r < 1 for stability), with y = –2 a:
Filter design programs use r as approximation of quality factor
  Real poles: b = 0 and 1 < a < 1, so r = |a| and y = 2 a and Q = ½ (impulse response is C0 an u[n] + C1 n a n u[n])
  Poles on unit circle: r = 1 so Q =  (oscillatory response)
  Imaginary poles: a = 0 so r = |b| and y = 0, and
  Processors with 16-bit x 16-bit multipliers and 40-bit accumulators: Qmax  40
Cascade of Biquads
Measures sensitivity in pole locations to perturbations

## Slide 19: Quality Factors for Analog Biquads
Second-order filter section
  Conjugate symmetric poles a ± j b, where a < 0
  With no zeros, impulse response is
  which is pure decay when b = 0 and pure sinusoid when a = 0
Quality factor: measures sensitivity of pole locations to perturbations
  Real poles: b = 0 so Q = ½ (exponential decay response)
  Imaginary poles: a = 0 so Q =  (oscillatory response)
  Maximum Q values: 25 for board-level RC circuits, 40 for switched capacitor designs, and 80 for analog IC designs
Classical designs have biquads with high Q factors
Cascade of Biquads

## Slide 20: IIR Filter as Single Section
IIR filters have rational transfer functions
Direct form realization
  Dot product of vector of N +1 coefficients and vector of current input and previous N inputs (FIR section)
  Dot product of vector of M coefficients and vector of previous M outputs (“FIR” filtering of previous output values)
  Computation: M + N + 1 multiply-accumulates (MACs)
  Memory: M + N words for previous inputs/outputs and M + N + 1 words for coefficients
Common IIR Filter Structures

## Slide 21: IIR Filter as Single Section

x[n]
y[n]
y[n-M]
x[n-1]
x[n-2]
b2
b1
b0
Unit Delay
Unit Delay
Unit Delay
x[n-N]
bN
Feed-forward
a1
a2
y[n-1]
y[n-2]
Unit Delay
Unit Delay
Unit Delay
aM
Feedback
M and N may be different
Full Precision Wordlength of y[0] is 2 words. Wordlength of y[n] increases with n for n > 0.
Common IIR Filter Structures

## Slide 22: Stability As Single Section
IIR filter design to meet a specification
  Manual or automatic placement of poles and zeros
  Poles are inside unit circle for stability
Factored transfer function in poles, zeros and gain
  Expanded to obtain coefficients for difference equation
  Expansion for feedback coefficients can lead to instability
Second-order example: zeros z0 & z1, poles p0 & p1
  Each addition and multiplication in 64-bit floating point
worst-case loss of one bit
worst-case loss of 53 bits

## Slide 23: Stability As Single Section

## Slide 24: MATLAB Filter Designer Demo #1
Filter design/analysis
Lowpass filter design specification (all demos)
  fpass = 9600 Hz
  fstop = 12000 Hz
  fsampling = 48000 Hz
  Apass = 1 dB
  Astop = 80 dB
Under analysis menu
  Show magnitude, phase and group delay responses
FIR filter – equiripple
  Also called Remez Exchange or Parks-McClellan design
  Minimum order is 50
  Change Wstop to 80
  Order 100 gives Astop 100 dB
  Order 200 gives Astop 175 dB
  Order 300 does not converge –how to get higher order filter?
FIR filter – Kaiser window
  Minimum order 101 meets spec
Cascade of Biquads

## Slide 25: MATLAB Filter Designer Demo #2
IIR filter – elliptic
  Use second-order sections
  Filter order of 8 meets spec
  Achieved Astop of ~80 dB
  Poles/zeros separated in angle
  Zeros on or near unit circle indicate stopband
  Poles near unit circle indicate passband
  Two poles very close to unit circle but still BIBO stable
  Show group delay response
IIR filter – elliptic
  Use second-order sections
  Increase filter order to 9
  Eight complex symmetric poles and one real pole:
  Same observations on left
Cascade of Biquads

## Slide 26: MATLAB Filter Designer Demo #3
IIR filter – elliptic
  Use second-order sections
  Increase filter order to 20
  Two poles very close to unit circle but BIBO stable
Single section (Edit menu)
  Oscillation frequency ~9 kHz appears in passband
  BIBO unstable: two pairs of poles outside unit circle
IIR filter design algorithms return poles-zeroes-gain (PZK format): Impact on response when expanding polynomials in transfer function from factored to unfactored form (see slide 6-25)
Cascade of Biquads

## Slide 27: MATLAB Filter Designer Demo #4
IIR filter - constrained least pth-norm design
  Use second-order sections
  Limit pole radii ≤ 0.92
  Order 8 does not meet both passband/stopband specs for different weights
Filter order might increase but worth higher complexity for being more robust perturbations in pole locations
  Order 9 does indeed meet specs using Wpass = 1.5 and Wstop = 800
Cascade of Biquads

## Slide 28: Conclusion
 | FIR Filters | IIR Filters
Implementation complexity (1) | Higher | Lower (sometimes by factor of four)
Minimum order design algorithm | Parks-McClellan (Remez exchange) algorithm (2) | Elliptic design algorithm
BIBO stable? | Always | May become unstable when implemented (3)
Linear phase | If impulse response is symmetric or anti-symmetric about midpoint | No, but phase may made approximately linear over passband (or other band)
(1) For same piecewise constant magnitude specification (2) Algorithm to estimate minimum order for Parks-McClellan algorithm by Jim Kaiser may be off by 10%. Search for minimum order is often needed. (3) Choice of IIR filter structure matters -- use cascade of biquads instead of a single section. Some IIR filter design algorithms can constrain pole locations.

## Slide 29: Conclusion
Keep poles computed by filter design algorithms
  Polynomial deflation (rooting) reliable in floating-point
  Polynomial inflation (expansion) may degrade roots
Direct form IIR structures expand zeros and poles
  May become unstable for large order filters (order > 12) due to degradation in pole locations from polynomial expansion
Cascade of biquads (second-order sections)
  Only poles and zeros of second-order sections expanded
  Biquads placed in order of ascending quality factors
  Optimal ordering of biquads requires exhaustive search and each ordering can be simulated in parallel for speed