## Slide 1: Quadrature Amplitude Modulation (QAM) Receiver
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin

## Slide 2: Introduction
Channel impairments
  Linear and nonlinear distortion of transmitted signal
  Additive noise (often assumed to be Gaussian)
Mismatch in transmitter/receiver analog front ends
Receiver subsystems to compensate for impairments
  Fading Automatic gain control (AGC)
  Additive noise Matched filters
  Linear distortion Channel equalizer
  Carrier mismatch Carrier recovery
  Symbol timing mismatch Symbol clock recovery

## Slide 3: Baseband QAM
L samples/symbol m sample index n symbol index
Receiver
Transmitter
Downconverted signal r1(t)
Carrier recovery is not shown
A/D
Symbol
Clock
Recovery
LPF
LPF
Carrier Detect
AGC
X
X
r1(t)
r(t)
r[m]
Channel Equalizer
L
L
QAM Demodulation
c(t)
2 cos(c m)
-2 sin(c m)
i[n]
gT[m]
L
+
cos(c m)
q[n]
gT[m]
L
sin(c m)
Serial/ parallel converter
1
Bits
Map to 2-D
constellation
J
Pulse shapers (FIR filters)
Index
s[m]
D/A
s(t)
fs

## Slide 4: Automatic Gain Control
Scales input voltage to A/D converter
  Increase/decrease gain for low/high r1(t)
A/D converter with 8-bit signed output
  When gain c(t) is zero, A/D output is 0
  When gain c(t) is infinity, A/D output is -128 or 127
  f-128, f0, f127 represent how frequently outputs -128, 0, 127 occur
  fi = ci / N where ci is count of times i occurs in last N samples
  Update #1: c(t) = (1 + 2 f0 – f-128 – f127) c(t – t)
  Update #2:
  Constant e > 0 prevents division by zero
A/D
AGC
r1(t)
r(t)
r[m]
c(t)
fs

## Slide 5: Channel Equalizer
Mitigates linear distortion in channel
When placed after A/D converter
  Time domain: shortens channel impulse response
  Frequency domain: compensates channel distortion over entire discrete-time frequency band instead of transmission band
Ideal channel
  Cascade of delay D and gain g
  Impulse response: impulse delayed by D with amplitude g
  Frequency response: allpass and linear phase (no distortion)
  Undo effects by discarding D samples and scaling by 1/g
z-
g

## Slide 6: Channel Equalizer
IIR equalizer
  Ignore noise nm
  Set error em to zero
  H(z) W(z) = g z-D
  W(z) = g z-D / H(z)
  Issues? See slide 6-15.
FIR equalizer
  Adapt equalizer coefficients when transmitter sends training sequence to reduce measure of error, e.g. square of em
Discrete-Time Baseband System
z-
h
+
w
-
xm
ym
em
rm
nm
+
Equalizer
Channel
g
Ideal Channel
+
Receiver generates xm
Training sequence

## Slide 7: Adaptive FIR Channel Equalizer
Simplest case: w[m] = d[m] + w1 d[m-1]
  Two real-valued coefficients w/ first coefficient fixed at one
z-
h
+
w
-
xm
ym
em
rm
nm
+
Equalizer
Channel
g
Ideal Channel
+
Receiver generates xm
Training sequence
sm
  Using least mean squares (LMS)
Derive update equation for w1 during training
  Step size 0 < m < 1

## Slide 8: Adaptive FIR Channel Equalizer
General case: Adapt N real coefficients w0, w1, … wN-1
Derive coefficient update equations during training
Vector form:

## Slide 9: Carrier Detection
Detect energy of received signal (always running)
  c is a constant where 0 < c < 1 and r[m] is received signal
  Let x[m] = r2[m]. What is the transfer function?
  What values of c to use?
If receiver is not currently receiving a signal
  If energy detector output is larger than a large threshold, assume receiving transmission
If receiver is currently receiving signal, then it detects when transmission has stopped
  If energy detector output is smaller than a smaller threshold, assume transmission has stopped

## Slide 10: Symbol Clock Recovery
Two single-pole bandpass filters in parallel
  One tuned to upper Nyquist frequency u = c + 0.5 sym
  Other tuned to lower Nyquist frequency l = c – 0.5 sym
  Bandwidth is B/2 (100 Hz for 2400 baud modem)
when
Lowpass IIR filter
Pole locations?
See Reader handout M
A recovery method
  Multiply upper bandpass filter output with conjugate of lower bandpass filter output and take the imaginary value
  Sample at symbol rate to estimate timing error 
  Smooth timing error estimate to compute phase advancement

## Slide 11: Baseband QAM Demodulation
  Recovers baseband in-phase/quadrature signals
  Assumes perfect AGC, equalizer, symbol recovery
QAM modulation followed by lowpass filtering
  Receiver fmax = 2 fc + B and fs > 2 fmax
Lowpass filter has other roles
  Matched filter
  Anti-aliasing filter
Matched filters
  Maximize SNR at downsampler output
  Hence minimize symbol error at downsampler output
LPF
LPF
X
X
2 cos(c m)
-2 sin(c m)
x[m]

## Slide 12: Baseband QAM Demodulation
QAM baseband signal
baseband
high frequency component centered at 2 wc
high frequency component centered at 2 wc
baseband
QAM demodulation
  Modulate and lowpass filter to obtain baseband signals