## Slide 1: Quadrature Amplitude Modulation (QAM) Transmitter
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin

## Slide 2: Introduction
Digital Pulse Amplitude Modulation (PAM)
  Modulates digital information (symbols) onto amplitude of pulse
  May be later upconverted (e.g. to radio frequency)
Digital Quadrature Amplitude Modulation (QAM)
  Two-dimensional extension of digital PAM
  Baseband signal requires sinusoidal amplitude modulation
  May be later upconverted (e.g. to radio frequencies)
Digital QAM modulates digital information onto pulses that are modulated onto
  Amplitudes of a sine and a cosine, or equivalently
  Amplitude and phase of single sinusoid

## Slide 3: Baseband PAM Transmitter
Bit stream to continuous-time pulse stream
  Group stream of bits into symbols of J bits
  Map symbol of J bits to unique symbol amplitude
  Interpolate from discrete-time to continuous-time
Serial/ Parallel
1
J
bit stream
J bits per symbol
Map to PAM
constellation
an
symbol amplitude
s*(t)
baseband waveform
Discrete-to-Continuous Time Conversion (Interpolation)
Pulse shaper gTsym[m]
L
Serial/ Parallel
1
J
Map to PAM
constellation
an
s*(t)
D/A
fs
@fs
@fs
@fsym
@fsym
fs = L fsym
4-PAM Map
d
d
3d
3d
00
01
10
11
symbol of bits
symbol ampl.
Review
L samples/symbol (upsampling factor)

## Slide 4: Amplitude Modulation by Cosine
y1(t) = x1(t) cos(wc t)
Review
Demodulation: modulation then lowpass filtering
  Assume x1(t) is an ideal lowpass signal with bandwidth w1
  Assume w1 < wc
  Y1(w) is real-valued if X1(w) is real-valued
w
0
1
w1
-w1
X1(w)
Baseband signal
½
Upconverted signal
w
0
Y1(w)
½
-wc - w1
-wc + w1
-wc
wc - w1
wc + w1
wc
½X1(w - wc)
½X1(w + wc)
1
See Slides 1-6 and 1-7

## Slide 5: Amplitude Modulation by Sine
y2(t) = x2(t) sin(wc t)
Review
w
0
1
w2
-w2
X2(w)
Baseband signal
Demodulation: modulation then lowpass filtering
  Assume x2(t) is an ideal lowpass signal with bandwidth w2
  Assume w2 < wc
  Y1(w) is imaginary-valued if X1(w) is real-valued
w
Y2(w)
j ½
-wc – w2
-wc + w2
-wc
wc – w2
wc + w2
wc
-j ½X2(w - wc)
j ½X2(w + wc)
-j ½
Upconverted signal
See Slides 1-8 and 1-9

## Slide 6: How to Use Bandwidth Efficiently?
+
cos(c t)
sin(c t)
x1(t)
x2(t)
s(t)
Cosine modulated signal is in theory orthogonal to sine modulated signal at transmitter
  Receiver separates x1(t) and x2(t) through demodulation
  Send two baseband signals in same transmission bandwidth
  Called Quadrature Amplitude Modulation (QAM)
  Used in DSL, cable, Wi-Fi, LTE
Sinusoidal mod doubles transmission bandwidth

## Slide 7: QAM Transmitter Architecture #1
Use D/A converter for each baseband PAM channel
i[n]
q[n]
Map to 2-D
constellation
Serial/ parallel converter
1
Bits
J
Index
D/A power consumption
4-level QAM Constellation
I
Q
d
d
-d
-d
+
s(t)
4-QAM is 2-PAM in the in-phase dimension and 2-PAM in the quadrature dimension
00
01
10
11
Pulse shaper gTsym[m]
L
D/A
fs
Pulse shaper gTsym[m]
L
D/A
B1
B1

## Slide 8: QAM Transmitter Architecture #2
Use only one D/A converter
Pulse shaper gTsym[m]
Pulse shaper gTsym[m]
Serial/ parallel converter
1
Bits
J
Index
Map to 2-D
constellation
i[n]
q[n]
L
L
4-level QAM Constellation
I
Q
d
d
-d
-d
00
01
10
11
D/A power consumption
4-QAM is 2-PAM in the in-phase dimension and 2-PAM in the quadrature dimension
+
cos(0 m)
sin(0 m)
s[m]
D/A
s(t)
fs
B2
B1
B1

## Slide 9: Comparison for 64-QAM (J=6 bits)
Serial/ parallel converter
1
Bits
6
Index
+
s(t)
D/A
fs
D/A
i[n] and q[n] are 8-PAM
symbol amplitudes, e.g. { -7, -5, -3, -1, 1, 3, 5, 7 } for d = 1 which needs 4 bits
Map to 2-D
constellation
i[n]
q[n]
4
4
Pulse shaper gTsym[m]
Pulse shaper gTsym[m]
4+Bp
4+Bp
Upsampling copies input sample to output and then L-1 zeros, and repeats
L
4
4
L
+
cos(0 m)
sin(0 m)
s[m]
D/A
s(t)
fs
B2
4+ Bp +Bf
4+ Bp+Bf
Bf fractional bits for each sinusoidal value
#1
#2
FIR filtering using Ng L coefficients has Ng non-zero multiplications due to upsampling. With C-bit FIR coefficients, FIR output will have
Bp
additional bits in worst case (see next slide)

## Slide 10: Wordlength Needed for Pulse Shaping

## Slide 11: Performance Analysis of PAM
If we sample matched filter output at correct time instances, nTsym, without any ISI, received signal
for i = -M/2+1, …, M/2
v(nT) ~ N(0; 2/Tsym)
4-level PAM Constellation
d
d
3 d
3 d
Matched filter has impulse response gr(t)
  where transmitted signal is
  v(t) output of matched filter Gr() for input of channel additive white Gaussian noise N(0; 2)
  Gr() passes frequencies from -sym/2 to sym/2 , where sym = 2  fsym = 2 / Tsym

## Slide 12: Performance Analysis of PAM
Decision error for inner points
-7d
-5d
-3d
-d
d
3d
5d
7d
O-
I
I
I
I
I
I
O+
8-level PAM Constellation
Decision error for outer points
Symbol error probability

## Slide 13: Performance Analysis of QAM
If we sample matched filter outputs at correct time instances, nTsym, without any ISI, received signal
4-level QAM Constellation
I
Q
d
d
-d
-d
Transmitted signal
  where i,k  { -1, 0, 1, 2 } for 16-QAM
Noise
  For error probability analysis, assume noise terms independent and each term is Gaussian random variable ~ N(0; 2/Tsym)
  In reality, noise terms have common source of additive noise in channel

## Slide 14: Performance Analysis of 16-QAM
Type 1 correct detection
3
3
3
3
2
2
2
2
2
2
2
2
1
1
1
1
I
Q
16-QAM
1 - interior decision region 2 - edge region but not corner 3 - corner region

## Slide 15: Performance Analysis of 16-QAM
Type 2 correct detection
3
3
3
3
2
2
2
2
2
2
2
2
1
1
1
1
I
Q
16-QAM
1 - interior decision region 2 - edge region but not corner 3 - corner region
Type 3 correct detection

## Slide 16: Performance Analysis of 16-QAM
Probability of correct detection
Symbol error probability (lower bound)
What about other rectangular QAM constellations?

## Slide 17: Examples
Determine decision regions for the receiver
  Draw boundaries at midpoint of every pair of constellation points
Rectangular constellations
  PAM in I and Q dimensions
  I and Q axes become boundaries
  Gray coding always possible

## Slide 18: Average Power Analysis
Assume each symbol is equally likely
Assume energy in pulse shape is 1
4-PAM constellation
  Amplitudes are in set { -3d, -d, d, 3d }
  Total power 9 d2 + d2 + d2 + 9 d2 = 20 d2
  Average power per symbol 5 d2
4-QAM constellation points
  Points are in set { -d – jd, -d + jd, d + jd, d – jd }
  Total power 2d2 + 2d2 + 2d2 + 2d2 = 8d2
  Average power per symbol 2d2
4-level PAM Constellation
d
-d
-3 d
3 d
4-level QAM Constellation
I
Q
d
d
-d
-d