## Slide 1: Generating Sinusoidal Signals
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
ECE 445S Real-Time Digital Signal Processing Lab Spring 2026
Lecture 1 http://www.ece.utexas.edu/~bevans/courses/realtime

## Slide 2: Outline
Bandwidth
Sinusoidal amplitude modulation
Sinusoidal generation
Design tradeoffs
Communication systems
  Wireless communication systems
  Software transceiver design

## Slide 3: Bandwidth
Non-zero extent in positive frequencies
Ideal Lowpass Spectrum
fmax
-fmax
f
Bandwidth fmax
Ideal Bandpass Spectrum
f1
f2
f
–f2
–f1
Bandwidth W = f2 – f1
Bandwidth
Applies to continuous-time & discrete-time signals
In practice, spectrum won’t be ideally bandlimited
  Thermal noise has “flat” power spectrum from 0 to 1015 Hz
  Finite observation time of signal leads to infinite bandwidth
Alternatives to “non-zero extent”?

## Slide 4: Bandwidth of Lowpass Signal in Noise
How to determine fmax?
Idealized Lowpass Spectrum
fmax
-fmax
f
Bandwidth
Lowpass Spectrum in Noise
f
approximate
Baseband signal: energy in frequency domain concentrated around DC
  Apply threshold and eyeball it
  OR
  Estimate fmax that captures certain percentage (say 90%) of energy
  In practice, (a) use large frequency in place of  and (b) integrate measured spectrum numerically

## Slide 5: Bandwidth of Bandpass Signal in Noise
How to find W = f2 – f1 ?
Idealized Bandpass Spectrum
f1
f2
f
–f2
–f1
Bandwidth
Bandpass Spectrum In Noise
f
fc
- fc
approximate
  Apply threshold and eyeball it
  OR
  Assume knowledge of fc and estimate f1 = fc  W/2 and f2 = fc + W/2 that capture percentage of energy
  In practice, (a) use large frequency in place of  and (b) integrate measured spectrum numerically

## Slide 6: Amplitude Modulation by Cosine
y1(t) = x1(t) cos(wc t)
w
0
Y1(w)
½
-wc - w1
-wc + w1
-wc
wc - w1
wc + w1
wc
½X1(w - wc)
½X1(w + wc)
lower sidebands
Sinuosidal Amplitude Modulation
  Assume x1(t) is ideal lowpass signal with bandwidth w1 < wc
  Amplitude modulation doubles baseband bandwidth of w1
  Y1(w) is real-valued if X1(w) is real-valued
See Slides 1-27, 3-6 and 15-6
w
0
1
w1
-w1
X1(w)
What are applications of amplitude modulation?

## Slide 7: Amplitude Demodulation by Cosine
How to recover x1(t) from y1(t) = x1(t) cos(wc t) ?
w
0
Y1(w)
½
-wc - w1
-wc + w1
-wc
wc - w1
wc + w1
wc
½X1(w - wc)
½X1(w + wc)
Sinuosidal Amplitude Modulation
F{ y1(t) cos(wc t) } = ½ Y1(w + wc) + ½ Y1(w – wc)
¼X1(w - 2wc)
¼X1(w + 2wc)
½ X1(w)
w
0
- 2wc+w1
-w1
-wc
w1
2wc- w1
wc
2wc
-2wc
2wc+w1
-2wc-w1
½
Homework 0.2
keep
attenuate
attenuate

## Slide 8: Amplitude Modulation by Sine
y2(t) = x2(t) sin(wc t)
Sinusoidal Amplitude Modulation
  Assume x2(t) is ideal lowpass signal with bandwidth w2 < wc
  Amplitude modulation doubles baseband bandwidth of w2
  Y2(w) is imaginary-valued if X2(w) is real-valued
w
0
1
w2
-w2
X2(w)
w
Y2(w)
j ½
-wc – w2
-wc + w2
-wc
wc – w2
wc + w2
wc
-j ½X2(w - wc)
j ½X2(w + wc)
-j ½
lower sidebands
See Slides 1-15, 3-6 and 15-6
Homework 0.1

## Slide 9: Amplitude Demodulation by Sine
How to recover x2(t) from y2(t) = x2(t) sin(wc t) ?
Sinusoidal Amplitude Modulation
w
Y2(w)
½ j
-wc – w2
-wc + w2
-wc
wc – w2
wc + w2
wc
-j ½X2(w - wc)
j ½X2(w + wc)
-½ j
0
- 2wc+w1
-w1
-wc
w1
2wc- w1
wc
2wc
-2wc
2wc+w1
-2wc-w1
w
½
F{ y2(t) sin(wc t) } = j ½ Y2(w +wc) – j ½ Y2(w –wc)
-¼X2(w - 2wc)
-¼X2(w + 2wc)
½ X2(w)
keep
attenuate
attenuate

## Slide 10: Sinusoidal Mod/Demod Demo #1
Sinusoidal Amplitude Modulation
Sinusoid of fixed frequency can model musical note
  Middle ‘A’ note on Western scale is at 440 Hz
  Signal model x1(t) = cos(2 p f1 t) where f1 = 440 Hz
cos(2 p fc t)
x1(t)
y1(t)
cos(2 p fc t)
LPF
y1(t)
x1(t)
^
v1(t)
Modulate middle ‘A’ note
  y1(t) = x1(t) cos(2 p fc t)
  fc is three octaves above f1
  Creates audio effect
Demodulate to try to recover original ‘A’ note
  Listen for frequencies in output signal that are not in original note

## Slide 11: Sinusoidal Mod/Demod Demo #1
(½)
(½)
(¼)
(¼)
(¼)
(¼)
f
X1(f)
f1
2f1
-f1
3f1
4f1
-2f1
5f1
-3f1
-4f1
-5f1
6f1
7f1
8f1
9f1
-6f1
-6f1
-7f1
-8f1
-9f1
f
Y1(f)
f1
2f1
-f1
3f1
4f1
-2f1
5f1
-3f1
-4f1
-5f1
6f1
7f1
8f1
9f1
-6f1
-6f1
-7f1
-8f1
-9f1
fc
- fc
(¼)
(¼)
(1/8)
(1/8)
(1/8)
(1/8)
f
V1(f)
f1
2f1
-f1
3f1
4f1
-2f1
-3f1
-4f1
15f1
17f1
-17f1
-15f1
2fc
-2fc
keep
attenuate
attenuate
Sinusoidal Amplitude Modulation

## Slide 12: Sinusoidal Mod/Demod Demo #1
%%% upconvert.m
%%%
%%% Demonstrates upconversion and downconversion
%%%
%%% by Prof. Brian L. Evans, bevans@ece.utexas.edu
%%% The University of Texas at Austin
%%%
%%% August 28, 2015
%%%
%%% This Matlab script will play three sounds:
%%% (1) low-frequency signal (baseband signal)
%%% (2) modulated signal centered at a higher frequency,
%%% (3) the demodulated signal,
%%% The demodulated signal consists of the baseband
%%% signal plus some higher frequency artifacts.
fs = 44100; %%% Sampling rate
Ts = 1/fs; %%% Sampling time
tmax = 10; %%% Signals last tmax seconds
t = 0 : Ts : tmax; %%% Vector of time samples
%%% Generate baseband signal
f1 = 440; %%% Middle 'A' on Western scale
basebandInput = cos(2*pi*f1*t);
%%% Modulate/upconvert baseband signal
%%% to be centered at frequency fc
fc = 8*f1; %%% 3 octaves above f1
carrier = cos(2*pi*fc*t);
modulated = basebandInput .* carrier;
%%% Demodulate/downconvert modulated signal
%%% 1. Modulate using the same carrier signal
%%% (causes gain to be reduced by 1/2)
%%% 2. Apply lowpass filter to extract baseband
%%% (and multiply by 2 of compensate for step 1)
%%% Use same carrier frequency fc as in modulation
carrier = cos(2*pi*fc*t);
modulateAgain = modulated .* carrier;
FIRlength = floor(fs/(2*f1));
lowpassCoeffs = ones(1, FIRlength) / FIRlength;
basebandOutput = 2*filter(lowpassCoeffs, 1, modulateAgain);
%%% Playback signals
sound(basebandInput, fs);
pause(tmax+1);
sound(modulated, fs);
pause(tmax+1);
sound(basebandOutput, fs);
Sinusoidal Amplitude Modulation
See handout on designing averaging filters

## Slide 13: Sinusoidal Mod/Demod Demo #2
%%% upconvertGong.m
%%%
%%% Demonstrates upconversion and downconversion
%%%
%%% by Prof. Brian L. Evans, bevans@ece.utexas.edu
%%% The University of Texas at Austin
%%%
%%% Original version: August 28, 2015
%%% Current version: February 5, 2016
%%%
%%% This Matlab script will play three sounds:
%%% (1) low-frequency signal (baseband signal)
%%% (2) upconverted signal centered at a higher frequency,
%%% (3) the downconverted signal,
%%% The downconverted signal consists of the baseband
%%% signal plus some higher frequency artifacts.
%%%
%%% Note: The gong.wav file must be on your path.
addpath('/Users/brianevans/Documents/Courses/SDRBook/SRD-MatlabFiles/SRD - MatlabFiles');
%%% Read gong signal
%%% Dominant frequencies 520 (C5), 630, and 660 Hz (E5) from
%%% plotting spectrum: plotspec(basebandInput, 1/fs)
%%% Maximum frequency of interest, f1, is 660 Hz.
[basebandInput, fs] = audioread('gong.wav');
basebandInput = basebandInput';
f1 = 660;
Ts = 1/fs; %%% Sampling time
numSamples = length(basebandInput);
n = 1 : numSamples;
t = n * Ts;
tmax = Ts * numSamples;
%%% Upconvert using sinusoidal amplitude modulation
%%% to be centered at frequency fc
fc = 4*f1;
carrier = cos(2*pi*fc*t);
modulated = basebandInput .* carrier;
Sinusoidal Amplitude Modulation

## Slide 14: Sinusoidal Mod/Demod Demo #2
%%% Downconvert by sinusoidal amplitude demodulation
%%% 1. Modulate using the same carrier signal
%%% (causes gain to be reduced by 1/2).
%%% Assume knowledge of carrier frequency fc
%%% used in modulation/upconversion.
%%% 2. Apply lowpass filter to extract baseband
%%% (and multiply by 2 of compensate for step 1).
%%% Use averaging lowpass filter of length N
%%% which has null bandwidth B = 2 pi / N.
%%% In sinusoidal amplitude demodulation, baseband
%%% bandwith in Hz is f1. We can the solve for
%%% N in B = 2 pi / N = 2 pi f1 / fs, which gives
%%% N = fs / f1 (converted to integer).
carrier = cos(2*pi*fc*t);
modulateAgain = modulated .* carrier;
FIRlength = floor(fs/f1);
lowpassCoeffs = ones(1, FIRlength) / FIRlength;
basebandOutput = 2*filter(lowpassCoeffs, 1, modulateAgain);
%%% Playback signals
sound(basebandInput, fs);
pause(tmax+1);
sound(modulated, fs);
pause(tmax+1);
sound(basebandOutput, fs);
Sinusoidal Amplitude Modulation
Baseband signal (gong)
Modulated signal
Demodulated signal
See handout on designing averaging filters

## Slide 15: How to Use Bandwidth Efficiently?
+
cos(c t)
sin(c t)
x1(t)
x2(t)
s(t)
Sinusoidal Amplitude Modulation
Cosine modulated signal is in theory orthogonal to sine modulated signal at transmitter
  Receiver separates x1(t) and x2(t) through demodulation
Quadrature Amplitude Modulation (QAM)
  Send two baseband signals in same transmission bandwidth
  Used in LTE, Wi-Fi, cable, …
Sinusoidal mod doubles transmission bandwidth

## Slide 16: Lab 2: Sinusoidal Generation
Sampling
Sinusoidal Generation
Output waveform
  Digital-to-analog (D/A) conversion
Expected outcomes are to understand
  Signal quality vs. run-time complexity tradeoffs
Compute sinusoidal waveform
  Math library function call
  Difference equation
  Lookup table

## Slide 17: Sampling
Two-sided discrete-time cosine (or sine) signal with fixed-frequency 0 in rad/sample has form
  cos(0 n)
Sinusoidal Generation
One-sided continuous-time analog-amplitude cosine of frequency f0 in Hz
  cos(2  f0 t)
  Sample at rate fs by substituting t = n Ts = n / fs
  cos(2  (f0 / fs) n)
  Discrete-time frequency 0 = 2  f0 / fs in units of rad/sample
  Example: f0 = 1200 Hz and fs = 8000 Hz, 0 = 3/10 
Homework 0.3
Sampling Theorem?

## Slide 18: Sampling Theorem
Continuous-time signal x(t) with frequencies no higher than fmax can be reconstructed from its samples x(n Ts) if samples taken at rate fs > 2 fmax
Realistic that x(t) has no freq. content above fmax ?
Sampling: Time-Domain Views
  Discrete-Time Output
  Sampled Analog Output
Models opening/closing of switch as multiplication by impulse train
HW 0.3
x(t)
t
Ts
Ts
Sinusoidal Generation

## Slide 19: Sampled Analog: Frequency Domain
Sampling replicates spectrum of continuous-time signal at integer multiples of sampling frequency
w
G(w)
ws
2ws
-2ws
-ws
w
X(w)
2pfmax
-2pfmax
Modulation by cos(2 s t)
Modulation by cos(s t)
HW 0.3
How to recover X(w)?
Sinusoidal Generation

## Slide 20: Algorithm #1: C Math Function cos
Uses double-precision floating-point arithmetic
No standard in C for internal implementation
Appropriate for desktop computing
  On desktop computer, accuracy is a primary concern, so additional computation is often used in C math libraries
  In embedded scenarios, implementation resources generally at premium, so alternate methods are typically employed
GNU Scientific Library (GSL) cosine function
  Function gsl_sf_cos_e in file specfunc/trig.c
  Version 1.8 uses 11th order polynomial over 1/8 of period
  20 multiply, 30 add, 2 divide and 2 power calculations per output value (additional operations to estimate error)
Design Tradeoffs in Generating Sinusoidal Signals

## Slide 21: Efficient Polynomial Implementation
Use 11th-order polynomial
  Direct form a11 x11 + a10 x10 + a9 x9 + ... + a0
  Horner's form minimizes number of multiplications
  a11 x11 + a10 x10 + a9 x9 + ... + a0 = ( ... (((a11 x + a10) x + a9) x ... ) + a0
Comparison
Realization | Multiply Operations | Addition Operations | Memory Usage
Direct form | 66 | 10 | 13
Horner’s form | 11 | 10 | 12
Design Tradeoffs in Generating Sinusoidal Signals

## Slide 22: Algorithm #2: Difference Equation
Difference equation with input x[n] and output y[n]
  y[n] = (2 cos 0) y[n-1] - y[n-2] + x[n] - (cos 0) x[n-1]
  From inverse z-transform of z-transform of cos(0 n) u[n]
  Impulse response gives cos(0 n) u[n]
  Similar difference equation for sin(0 n) u[n]
Initial conditions are all zero
Design Tradeoffs in Generating Sinusoidal Signals
Implementation complexity
  Computation: 2 multiplications and 3 additions per cosine value
  Memory Usage: 2 coefficients, 2 previous values of y[n] and 1 previous value of x[n]
Drawbacks
  Buildup in error as n increases due to feedback
  Fixed value for 0
HW 0.4

## Slide 23: Differential Equation Drawbacks
If implemented with exact precision coefficients and arithmetic, output would have perfect quality
Accuracy loss as n increases due to feedback from
  Coefficients cos(0) and 2 cos(0) are irrational, except when cos(0) is equal to -1, -1/2, 0, 1/2, and 1
  Truncation/rounding of multiplication and addition results
Reboot filter after each period of samples by resetting filter to its initial state
  Reduce loss from truncating/rounding multiplication-addition
  Adapt/update 0 if desired by changing cos(0) and 2 cos(0)
Design Tradeoffs in Generating Sinusoidal Signals

## Slide 24: Algorithm #3: Lookup Table
Precompute samples offline and store them in table
Cosine frequency 0 = 2  f0 / fs = 2  N / L
  Remove common factors between integers N & L
  cos(2  f0 t) has continuous-time period T0 = 1 / f0
  cos(2  (N / L) n) has discrete-time period of L samples
Design Tradeoffs in Generating Sinusoidal Signals
Handout on discrete-time periodicity
N=3 continuous-time periods
Discrete-time period of L=20 samples

## Slide 25: Design Tradeoffs
Signal quality vs. run-time complexity in generating cos(0 n) where 0 = 2  f0 / fs = 2  N / L
Algorithm | MACs/ sample | ROM (words) | RAM (words) | Quality in floating pt. | Quality in fixed point
C math library call | 30 | 22 | 1 | Second Best | N/A
Difference equation | 2 | 2 | 3 | Worst | Second Best
Lookup table | 0 | L | 0 | Best | Best
MAC Multiplication-accumulation RAM Random Access Memory (writeable) ROM Read-Only Memory
Design Tradeoffs in Generating Sinusoidal Signals

## Slide 26: Communication System Structure
Information sources
  Voice, music, images, video, and data (message signal m(t))
  Have power concentrated near DC (called baseband signals)
Baseband processing in transmitter
  Lowpass filter message signal (e.g. AM/FM radio broadcast)
  Digital: Add redundancy to message bit stream to aid receiver in detecting and possibly correcting bit errors
Communication Systems
Received Message
Message
Baseband Processing
Analog/RF Front End
Transmission Medium
Analog/RF Front End
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL

## Slide 27: Transmitter Analog/RF Front End
Wireless Communication Systems
Received Message
Message
Baseband Processing
Analog/RF Front End
Transmission Medium
Analog/RF Front End
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL
Mixer: Reduce circuit complexity by replacing multiplication by cosine with sampling device (single transistor)
cos(2 p fc t)
D/A
fs
LPF
LNA
BPF
BPF selects replica of baseband spectrum at fc
LNA Low-Noise Amplifier
Wavelength l = c / fc
Antenna Length?

## Slide 28: Communication Channel Modeling
Wireless Communication Systems
Received Message
Message
Baseband Processing
Analog/RF Front End
Transmission Medium
Analog/RF Front End
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL
Line of sight
Propagation Paths
One bounce
Two bounces
Channel Impairments
Each path has its own attenuation and delay
Frequency distortion due to multiple paths
Additive thermal noise & interference
More in Lecture 12

## Slide 29: Receiver Analog/RF Front End
Wireless Communication Systems
Received Message
Message
Baseband Processing
Analog/RF Front End
Transmission Medium
Analog/RF Front End
Baseband Processing
TRANSMITTER
RECEIVER
s(t)
r(t)
CHANNEL
cos(2 p fc t)
A/D
fs
BPF
LNA
LPF
Mixer: Reduce circuit complexity by replacing multiplication by cosine with sampling device (single transistor)
LPF selects replica of bandpass spectrum at baseband
LNA Low-Noise Amplifier

## Slide 30: Software Transceiver Design
Design/implement transceiver
  Design/evaluate algorithms for each subsystem
  Translate algorithms into real-time software
  Test implementations using signal generators & oscilloscopes
Software Transceiver Design
general signal processing building blocks