## Slide 1: Signals and Systems

## Slide 2: Outline
Signals
  Continuous-time vs. discrete-time
  Analog vs. digital
  Unit impulse
1
-1
Continuous-Time System Properties
Sampling
Discrete-Time System Properties

## Slide 3: Many Faces of Signals
Function, e.g. cos(t) in continuous time or cos(p n) in discrete time, useful in analysis
Review
Sequence of numbers, e.g. {1,2,3,2,1} or a sampled triangle function, useful in simulation
Set of properties, e.g. even and causal, useful in reasoning about behavior
A piecewise representation, e.g. useful in analysis
A generalized function, e.g. d(t), useful in analysis

## Slide 4: Signals As Functions
Continuous-time x(t)
  Time, t, is any real value
  x(t) may be 0 for range of t
Review
Analog Amplitude Signal  Quantizer  Digital Amplitude Signal
Continuous-Time Signal  Sampler  Discrete-Time Signal
Discrete-time x[n]
  n  {...-3,-2,-1,0,1,2,3...}
  Integer time index, e.g. n
Digital amplitude
  From discrete set of values
Analog amplitude
  Real or complex value
1
-1

## Slide 5: Continuous-Time Unit Impulse
Mathematical idealism for an instantaneous event
e
-e
t
Unit Area
Review
t
(1)
0
Unit Area
Dirac delta as generalized function (a.k.a. functional)
Selected properties
  Unit area:
  Sifting:
  provided g(t) is defined at t = 0
(0) is infinity or undefined (both are defensible answers)

## Slide 6: Continuous-Time Unit Impulse
d(t) under integration
Review
L. B. Jackson, “A correction to impulse invariance,” IEEE Sig. Proc. Letters, Oct. 2000.
What about?
  Assuming (t) is defined at t=0
What about at origin?
  u(0) can take any value
  Common values: 0, ½, 1
Other examples
What about?
  By substitution of variables,

## Slide 7: Systems
Systems operate on signals to produce new signals or new signal representations
Review
Squaring function can be used in sinusoidal demodulation
Average of current input and delayed input is a simple filter
T{•}
y(t)
x(t)
T{•}
y[n]
x[n]
Continuous-time system examples
  y(t) = ½ x(t) + ½ x(t-1)
  y(t) = x2(t)
Discrete-time system examples
  y[n] = ½ x[n] + ½ x[n-1]
  y[n] = x2[n]

## Slide 8: Continuous-Time System Properties
Let x(t), x1(t), and x2(t) be inputs to a continuous-time linear system and let y(t), y1(t), and y2(t) be their corresponding outputs
Review
Quick test to identify some nonlinear systems?
A linear system satisfies
  Additivity: x1(t) + x2(t)  y1(t) + y2(t)
  Homogeneity: a x(t)  a y(t) for any real/complex constant a
For time-invariant system, shift of input signal by any real-valued t causes same shift in output signal, i.e. x(t - t)  y(t - t), for all t

## Slide 9: Why are LTI properties useful?
An LTI system is uniquely characterized by its impulse response
  Abstract away implementation details by providing an impulse response e.g. to hide intellectual property
  Model unknown system (even though it might not be LTI)
Fourier transform of the impulse response h(t) is the frequency response of the system Hfreq(f)
h(t)
x(t)
y(t) = h(t) * x(t)
Time domain
X(s)
Y(s) = H(s) X(s)
Laplace domain
Xfreq(f)
Yfreq(f) = Hfreq(f) Xfreq(f)
Frequency domain

## Slide 10: Is a System Linear or Not?
()2
y(t)
x(t)
Example: Squaring block
  Does the squaring block pass all-zero input test?
  Does the squaring block have homogeneity?
y(t)
x(t)
()2
a x(t)
yscaled(t)
  Check to see if yscaled(t) = a y(t) for all constant values of a
y(t) = x2(t)
  (a x(t))2 = a x2(t)
yscaled(t) = (a x(t))2
  a2 x2(t) = a x2(t)
  only for a = 0 and a = 1
No

## Slide 11: Is a System Time-Invariant or Not
()2
y(t)
x(t)
Example: Squaring block
  Does shift in time for input always give same shift on output?
y(t)
x(t)
()2
x(t-t0)
yshifted(t)
  Check to see if yshifted(t) = y(t-t0) for all real values of t0
y(t) = x2(t)
  (x(t-t0))2 = x2(t-t0)
yshifted(t) = (x(t-t0))2
  x2(t-t0) = x2(t-t0)
Yes
All pointwise systems are time-invariant
  Output at time t only depends on input at time t

## Slide 12: Initial Conditions for Linear Systems
Observe signals and systems starting at time t = 0
x(t)
y(t)
C0 is the initial condition w/r to observation
Example: Integrator
Observe integrator for t  0
System “at rest” is a necessary condition for linearity
x(t)
y(t)
  Homogeneity: input for output
  for all values of ?

## Slide 13: Init. Cond. for Time-Invariant Systems?
Observe system for t  0-
  Does yshifted(t) = y(t-t0) for all real-valued t0 for ?
  Notation means to include any Dirac delta signals at origin
Handouts for example systems
  Time-Invariance for a (Shift) System Under Observation
  Time-Invariance for an Integrator
link
link

## Slide 14: Continuous-Time System Properties
Ideal delay by T seconds
x(t)
y(t)
x(t)
y(t)
x(t)
y(t)
Role of initial conditions?
Scale by a constant (a.k.a. gain block)
  Two different ways to express it in a block diagram
  Linear? Time-invariant?
  Linear? Time-invariant?

## Slide 15: Continuous-Time System Properties
Tapped delay line
M-1 delay blocks
S
…
…
Coefficients a0, a1, …aM-1
Role of initial conditions?
Impulse response h(t) lasts (M-1)T seconds:
  Linear? Time-invariant?
y(t) = a0 x(t) + a1 x(t – T) + … + aM-1 x(t – (M-1)T)
h(t)
T
(M-1)T
(a1)
(a0)
(aM-1)
t
…

## Slide 16: Continuous-Time System Properties
Amplitude Modulation (AM)
  y(t) = A x(t) cos(2p fc t)
  fc carrier frequency
  A is a constant
A
x(t)
cos(2 p fc t)
y(t)
AM radio if x(t) = 1 + ka m(t) where m(t) is audio to be broadcast and |ka m(t)| < 1 (see lecture 19)
  Linear? Time-invariant?
Linearity: Does system pass all-zero input test?
y(t)
x(t)
a x(t)
yscaled(t)
y(t) = A x(t) cos(2p fc t)
yscaled(t) = A (a x(t)) cos(2p fc t)
yscaled(t) = a (A x(t) cos(2p fc t)) = a y(t) for all constants a

## Slide 17: Discrete-Time Signals
Conversion of signals
  Sampling: Continuous-Time to Discrete-Time
  Reconstruction: Discrete-Time to Continuous-Time
f0 = 440;
fs = 24*f0;
Ts = 1/fs;
tmax = 1/f0;
t = 0 : Ts : tmax;
x = cos(2*pi*f0*t);
plot(t, x);
figure;
stem(t, x);
cosine at 440 Hz
t
sampling rate: 10560 Hz sampling period: 94.7 ms
sampling
reconstruction
Review

## Slide 18: Generating Discrete-Time Signals
Many signals originate in continuous time
  Example: Talking on cell phone
Sampled analog waveform
s(t)
t
Ts
Ts
Review
n
d[n]
1
1
-1
2
3
-2
-3
Sample continuous-time signal at equally-spaced points in time to obtain a sequence of numbers
  s[n] = s(n Ts) for n  {…, -1, 0, 1, …}
  How to choose sampling period Ts ?
Using a formula
  Discrete-time impulse d[n] on right
  How does d[n] look in continuous time?

## Slide 19: Aliasing Example
Sample 30 kHz sinusoid using 48 kHz sampling rate

## Slide 20: Discrete-Time System Properties
Let x[n], x1[n] and x2[n] be inputs to a linear system
Let y[n], y1[n] and y2[n] be corresponding outputs
A linear system satisfies
  Additivity: x1[n] + x2[n]  y1[n] + y2[n]
  Homogeneity: a x[n]  a y[n] for any real/complex constant a
For a time-invariant system, a shift of input signal by any integer-valued m causes same shift in output signal, i.e. x[n - m]  y[n - m], for all m
Role of initial conditions?
Review

## Slide 21: Why are LTI properties useful?
An LTI system is uniquely characterized by its impulse response
  Abstract away implementation details by providing an impulse response e.g. to hide intellectual property
  Model an unknown system assumed to be LTI
Fourier transform of the impulse response h[n] is the frequency response of the system Hfreq(w)
h[n]
x[n]
y[n] = h[n] * x[n]
Time domain
X(z)
Y(z) = H(z) X(z)
Z domain
Xfreq(w)
Yfreq(w) = Hfreq(w) Xfreq(w)
Frequency domain

## Slide 22: Discrete-Time System Properties
Tapped delay line in discrete time
M-1 delay blocks where z-1 is delay of 1 sample:
S
…
…
See also slide 5-4
Coefficients a0 a1…aM-1 are impulse response:
Role of initial conditions?
Linear? Time-invariant?
h[n]
n
-1
2
M-1
M
…
1
a0
a1
aM-1

## Slide 23: Averaging Filter
Continuous time
  Averages input signal over previous T seconds
See Designing Averaging Filters Handout
Linear? Time-invariant?
Linear? Time-invariant?
Hint: Tapped delay line with am = 1/M for m in [0, M-1]
Discrete time
  Averages current and previous M-1 samples
0
T
t
h(t)
Impulse response:
n
h[n]
1
-1
2
M-1
M
…
0

## Slide 24: First-Order Difference Filter
Continuous time
f(t)
y(t)
f[n]
y[n]
See also slide 5-19
Linear? Time-invariant?
Linear? Time-invariant?
Hint: Tapped delay line with a0 = 1 and a1 = -1
Discrete time