## Slide 1: Sampling and Aliasing

## Slide 2: Outline
w
G(w)
ws
2ws
-2ws
-ws
f(t)
t
Ts
Ts
g(t)
Sampling
  Time domain views
  Frequency domain view
  Sampling theorem
Conclusion
Aliasing
  Sinusoidal example
  Bandpass sampling

## Slide 3: Sampling
Analog-to-Digital Conversion
  Lowpass filter has stopband frequency less than ½ fs to reduce aliasing at sampler output (enforce sampling theorem)
Sampling – Time Domain View
Sampling: Time-Domain Views
Analog Lowpass Filter
Quantizer
Sampler at sampling rate of fs
x(t)
  Discrete-Time Output
  Sampled Analog Output
x(t)
t
Ts
Ts
Models opening/closing of switch as multiplication by impulse train
HW 0.3
Today
Lecture 8

## Slide 4: Sampled Analog: Frequency Domain
Sampling replicates spectrum of continuous-time signal at integer multiples of sampling frequency
w
G(w)
ws
2ws
-2ws
-ws
w
X(w)
2pfmax
-2pfmax
Modulation by cos(2 s t)
Modulation by cos(s t)
Sampling – Frequency Domain View
HW 0.3
How to recover X(w)?

## Slide 5: Sampling Theorem
Continuous-time signal x(t) with frequencies no higher than fmax can be reconstructed from its samples x(n Ts) if samples taken at rate fs > 2 fmax
  Nyquist rate = 2 fmax
  Nyquist frequency = fs / 2 maximum frequency captured
What happens after sampling to fmax = ½ fs ?
x(t) = cos(2 p fmax t)
y(t) = sin(2 p fmax t)
Sampling - Review
Aliasing
Highest DT Frequency
gives
y[n] = sin(p n) = 0
Unrealistic: x(t) has no frequency content above fmax

## Slide 6: Sample-and-Hold Reconstruction
Sampling theorem gives condition for which reconstruction is possible but not how to do it
t
x[n]
1
2
-1
3
4
5
6
n
0
…
…
x(t)
^
0
Ts
1
t
p(t)
Linear systems approaches for reconstruction
  Ideal lowpass filter with two-sided sinc impulse response
  No unique filtering approach for reconstruction in practice
  Sample-and-hold approach below has efficient implementation
Ts
0
-Ts
2Ts
3Ts
…
…
Sampling - Reconstruction

## Slide 7: Sampling and Oversampling Demo
As sampling rate increases above Nyquist rate, sampled waveform looks more like original
Sampling
link
Zero crossings: frequency content of a sinusoid
  Distance between two zero crossings: one half period
DSP First, 2nd ed., ch. 4, sampling/interpolation
  With sampling theorem satisfied, sampled sinusoid crosses zero right number of times per period
  In some applications, frequency content matters not shape of time-domain waveform
t

## Slide 8: Aliasing: Sinusoidal Example
Sample x(t) at fs = 48 kHz
  x(t) = cos(2 p f0 t) where f0 = 30 kHz
Aliasing
(½)
(½)
f
X(f)
6
kHz
12
18
24
30
36
42
48
-6
-12
-18
-24
-30
-36
-42
-48
(½ fs)
(½fs)
f
Y(f)
6
kHz
12
18
24
30
36
42
48
-6
-12
-18
-24
-30
-36
-42
-48
(½fs)
(½fs)
Reconstruction uses -½ fs < f < ½ fs
x(t)
y(t)
fs
See slides 3-19 & 4-4
  Y(f) has X(f) plus replicas of X(f) at offsets of multiples of fs
Effective freq. 18 kHz

## Slide 9: Increasing Sampling Rates
Consider adding speech clip to an audio track
  Speech signal s[n] is sampled at 8 kHz
  Audio signal r[m] is sampled at 48 kHz
Digital to Analog Converter
Analog to Digital Converter
8000 Hz
48000 Hz
s[n]
+
r[m]
FIR Filter
6
s[n]
+
r[m]
Upsampling
Interpolation
Efficient approach: Interpolate in discrete time
Inefficient approach: Interpolate in continuous time

## Slide 10: Increasing Sampling Rates
Upsampling by L
  Copies input sample to output and appends L-1 zeros
  Output has L times as many samples as input samples
FIR Filter
6
x[n]
Upsampling
Interpolation
v[m]
y[m]
Audio Demonstration
  Plots/plays x[n] which is a 600 Hz cosine sampled at 8000 Hz
  Plots/plays v[m]: spectrum is spectrum of x[n] plus L-1 replicas
  Interpolation filter fills in inserted zero values in time domain and attenuates replicas in frequency domain due to upsampling
  Rectangular, triangular and truncated sinc FIR filters used

## Slide 11: Bandpass Sampling
Uses aliasing to our benefit
Reduce sampling rate
  Bandwidth f2 – f1
  Sampling rate fs > f2 – f1
  For replica to be centered at origin after sampling fcenter = ½(f1 + f2) = k fs
Ideal Bandpass Spectrum
f1
f2
f
–f2
–f1
Sample at fs
Sampled Ideal Bandpass Spectrum
f1
f2
f
–f2
–f1
Lowpass filter to extract baseband
Aliasing
Practical issues
  Sampling clock tolerance: fcenter = k fs
  Bandpass and lowpass filter designs
  Effects of noise

## Slide 12: Bandpass Sampling Example
Ideal Bandpass Spectrum S(f)
f1
f2
f
–f2
–f1
Bandpass sampling
  Bandwidth f2 – f1
  fs > f2 – f1
  fcenter = ½(f1 + f2) = k fs
Extract IEEE 802.11a Wi-Fi 2.4 GHz Channel 1
  f1 = 2.401 GHz
  f2 = 2.423 GHz
  Bandwidth = 0.022 GHz
  fc = 2.412 GHz
Sampling theorem
  fs > 2 f2 e.g. fs = 4.86 GHz
Bandpass sampling
  fs = 0.036 GHz with k = 67
  135x more efficient
Aliasing
Sample at rate fs
Bandpass Filter
Lowpass Filter

## Slide 13: Software Defined Radio
Worldwide unlicensed microwave band at 2.4 GHz
  Any service can use this band but must follow regulations on transmit power, out-of-band leakage, etc.
  Services include Bluetooth, Wi-Fi, wireless mice/keyboards, ZigBee, baby monitors, wireless microphones/speakers
Aliasing
f
0
-f2
-f1
-fc
f1
f2
fc
Extract band for processing
  f1 = 2.4 GHz
  f2 = 2.5 GHz
  BW = 0.1 GHz
  Bandpass sampling with fs = 0.2 GHz
f
0
BW
- BW
25x more efficient vs. fs = 5 GHz

## Slide 14: Software Defined Radio

## Slide 15: Conclusion
Sampling replicates spectrum of continuous-time signal at offsets that are integer multiples of sampling frequency
Sampling theorem gives necessary condition to reconstruct the continuous-time signal from its samples, but does not say how to do it
Aliasing occurs due to sampling
  Noise present at all frequencies
  A/D converter design tradeoffs to control impact of aliasing
Bandpass sampling reduces sampling rate significantly by using aliasing to our benefit

## Slide 16: Rolling Shutter Cameras
Smart phone and point-and-shoot cameras
  No (global) hardware shutter to reduce cost, size, weight
  Light continuously impinges on sensor array
  Artifacts due to relative motion between objects and camera
Figure from a tutorial by Forssen et al. at the 2012 IEEE Conf. on Computer Vision & Pattern Recognition
Optional

## Slide 17: Rolling Shutter Artifacts
Plucked guitar strings – global shutter camera
  String vibration is (correctly) damped sinusoid vs. time
C. Jia and B. L. Evans, “Probabilistic 3-D Motion Estimation for Rolling Shutter Video Rectification from Visual and Inertial Measurements,” IEEE Multimedia Signal Proc. Workshop, 2012. Link to article.
Warped frame
Compensated using gyroscope readings (i.e. camera rotation) and video features
video
video
“Guitar Oscillations Captured with iPhone 4”
  Rolling shutter (sampling) artifacts but not aliasing effects
Fast camera motion
  Pan camera fast left/right
  Pole wobbles and bends
  Building skewed
Optional