## Slide 1
Towards Power-Efficient and Intelligent Wireless Communication Systems
PhD Committee
Prof. Jeffrey G. Andrews
Prof. Brian L. Evans (Supervisor)
Prof. Grani Hanasusanto
Prof. Hyeji Kim
Prof. Aryan Mokhtari
June. 7, 2023
Yunseong Cho (yscho@utexas.edu)

## Slide 2: Outline
Motivation
Review of Contribution #1: Coordinated Beamforming and Power Control for Low-Resolution Systems: Total Power Minimization
Contribution #2: Coordinated Per-Antenna Maximum Power Minimization for Low-Resolution Systems
Contribution #3: Learning-Based Maximum Likelihood Detection with One-Bit ADCs
Contribution #4: Joint Hybrid Beamforming and Power Control Using Deep Reinforcement Learning
Conclusion and Future Works

## Slide 3: VISION FOR 6G COMMUNICATIONS
4G 5G
Latency
Data Traffic
Peak Data Rate
Sustainable Data Rate
Connectivity
10 ms
7.2 EB/mo
1 Gb/s
10 Mb/s
100k/km2
<1 ms
50 EB/mo
20 Gb/s
100 Mb/s
1M/km2
[1] https://www.qorvo.com/design-hub/blog/getting-to-5g-comparing-4g-and-5g-system-requirements
[2] Qualcomm, “It’s 2022 — why and what do you need to know about 6G?”
3GPP Release 18
Beamforming, power control, data detection
for low-power *MIMO systems
*MIMO: Multiple-Input Multiple-Output
Notes: [45s] From 4G to 5G, we have achieved many key performance indicators such as latency and data rates.
Now, we are looking at 6G communications to unlock a variety of application spaces.
In the meantime, 3GPP specifies possible research directions that can help us deploy 5G advanced or 6G in practice.
Out of the six items, I will contribute to these three topics by developing beamforming, power control, and data detection mechanism for low-power MIMO systems

## Slide 4: Motivation: Increased Power Consumption of Massive MIMO Systems
#1: Low-resolution data converters
Replace high-res data converters with low-res data converters
Power consumption is exponential in the number of quantization bits ().
Non-trivial quantization error
#2: Hybrid beamforming architecture
Use analog beamformer to project high-dim. input onto low-dim. output.
Directly scale down # of RF chains
Non-convex unit-modulus constraint of analog beamformers
Notes: The main motivation of my PhD research is the increased power consumption of massive MIMO systems.
To accomplish significant gain in data rates and compensate propagation loss by using beamforming, modern and future communication systems are coupled with Massive MIMO systems.
As we increase the number of antennas, we end up with the increased number of power hungry RF chains.
Therefore, we can come up with two possible low-power architectures.

## Slide 5: Contributions
2-4 bits
1-bit
Coordinated Beamforming & Power Control
Total Power
Minimization
Peak Power
Minimization
Learning-based
Data Detection
#1
#2
#3
*DRL-based Hybrid Beamforming
#4
#1: Low-resolution data converters
#2: Hybrid beamforming architecture
*DRL: Deep Reinforcement Learning

## Slide 6: Coordinated Beamforming and Power Control for Low-Resolution Systems: Total Power Minimization
Review of Contribution #1
Contribution #1: Coordinated Beamforming and Power Control for Low-Resolution Systems: Total Power Minimization
[1] Yunseong Cho, Jinseok Choi, and Brian L. Evans, “Coordinated Multicell Beamforming and Power Allocation for Massive MIMO with low-resolution ADC/DAC”, IEEE International Conference on Communications (ICC), Jun. 2021
[2] Jinseok Choi, Yunseong Cho, and Brian L. Evans, “Quantized Massive MIMO Systems with Multicell Coordinated Beamforming and Power Control”, IEEE Transactions on Communications, vol. 69, no. 2, pp. 946-961, Nov. 2020

## Slide 7: Background
Problem: Minimize total transmit power with target *SQINR
  Quantization noise from low-resolution (low-power) ADCs and DACs
  Thermal noise as well as intra-cell, and inter-cell interference
Quantized received signal in uplink
Quantized received signal in downlink
when transmits
inter-cell interference
Design uplink power control
Design downlink beamformer
quantization gain 1
inter-cell interference
+ inter-user interference
Solution: Opt. power control (uplink) & beamformer (downlink)
  Linearize coarse quantization as quantization gain and quantization noise via *AQNM, i.e.,
  Minimize uplink & downlink total transmit power with target SQINR
  Use strong duality between our uplink and downlink formulations
quantization noise
*SQINR: Signal-to-quantization-plus-interference-plus-noise ratio
*AQNM: Additive Quantization Noise Model
Contribution #1: Coordinated Beamforming and Power Control for Low-Resolution Systems: Total Power Minimization

## Slide 8
Uplink Total Transmit Power Minimization Problem
Theorem 1: Duality
Corollary 1: Strong Duality
Optimal Uplink Solution
covariance matrix of received signal
locally estimated w/o explicit inter-cell channels!!
distributed manner
Optimal Downlink Solution
computed from uplink solution and channel
computed from and
Downlink Total Transmit Power Minimization Problem
separate
problems
Derived Results and Proposed Algorithm
Contribution #1: Coordinated Beamforming and Power Control for Low-Resolution Systems: Total Power Minimization
1) Initialize
2) Iteratively update until converges
3) Find uplink MMSE equalizer using
4) Compute downlink beamformer
Proposed Algorithm (NB)
1) Initialize
2) Iteratively update until converges
3) Find uplink MMSE equalizer using
4) Compute downlink beamformer
Proposed Algorithm (WB)
: proved the same results in wideband case
convergence is also proved!!

## Slide 9: Simulation Results for the Proposed Iterative Coordinated Multipoint (iCoMP)
cells
users per cell
Target SINR vs. Total Transmit Power ( quantization bits)
gain over per-cell method
64 antennas, 7 cells, 4 users per cell, ,
CDF of achieved SINR
Distributed algorithms
Contribution #1: Coordinated Beamforming and Power Control for Low-Resolution Systems: Total Power Minimization
Notes: Let’s move onto the simulation results.
we plot target SINR versus total transmit power, and b means the number of quantization bits
We compare our algorithm against a per-cell approach. Red line are our algorithm and blue line are the per-cell approach.
With 16 antennas, the per-cell approach easily diverges in low-SINR target, however our method diverges in medium SINR.
With 128 antennas which is considered as massive MIMO, our method shows divergence only with 2 bits case.
This figure validates the strong duality between UL and DL. We first plot the uplink cases with red lines, and we placed the downlink results with blue markers. Since they are matching together, we can observe the strong duality from this figure,
For the wideband case, we have 16 antennas, 2 cells, 2 users per cell, and 64 subcarriers. We observed the same trend as narrowband case. The total transmit power increases as resolution decreases, but not very much.

## Slide 10: Coordinated Per-Antenna Maximum Power Minimization for Low-Resolution Systems
Contribution #2
Contribution #2: Coordinated Per-Antenna Maximum Power Minimization for Low-Resolution Systems
[1] Yunseong Cho, Jinseok Choi, and Brian L. Evans, “Coordinated Per-Antenna Power Minimization for Multicell Massive MIMO Systems with Low-Resolution Data Converters”, submitted to IEEE Transactions on Communications.
[2] Yunseong Cho, Jinseok Choi, and Brian L. Evans, “Coordinated Beamforming in Quantized Massive MIMO Systems with Per-Antenna Constraints”, IEEE Wireless Communications and Networking Conference (WCNC), Apr. 2022

## Slide 11: Motivation: Maximum Power Minimization
Per-Antenna Level Power Constraints
  Limit antenna powers to achieve energy efficiency and realistic deployment
  Avoid nonlinear and inefficient power amplification
  Place less burden on power amplifiers and electronics
[1] A. Vasjanov and V. Barzdenas, “A Review of Advanced CMOS RF Power Amplifier Architecture Trends for Low Power 5g Wireless Networks”, Electronics, vol. 7, no. 11, 2018
Contribution #2: Coordinated Per-Antenna Maximum Power Minimization for Low-Resolution Systems
Notes: Generally speaking, massive MIMO or large-scale antenna systems are one of the key technologies that enable modern and future communication systems because of its significant gain in spectral efficiency and capacity.
However, since each antenna is usually equipped with an RF chain with two 16-bit data converters, overall power consumption eventually goes up dramatically.
As one of the low-power solutions, we can choose to deploy low-resolution ADCs and DACs with typically 2 to 4 bits since power increases exponentially with the number of quantization bits.
On top of that, there is a need to limit the power of base stations to achieve more power-efficient deployment. In this way, we can place less burden on power amplifiers and electronic components.

## Slide 12: Background
Problem: Minimize maximum transmit power with target SQINR
  Quantization noise from low-resolution (low-power) ADCs and DACs
  Thermal noise as well as intra-cell, and inter-cell interference
  Per-antenna level power constraints
Solution: Opt. power control (uplink) & beamformer (downlink)
  Minimize peak transmit power with target SQINR
  Use strong duality between our uplink and downlink formulations
  Iterative optimization between uplink and downlink solutions
Contribution #2: Coordinated Per-Antenna Maximum Power Minimization for Low-Resolution Systems

## Slide 13: Problem Formulation
Maximum Transmit Power Minimization
Uplink (Dual)
Maximum Transmit Power Minimization
Downlink (Primal)
Limit antenna powers for efficiency
Place less burden on electronics
1. Find the inner problem solution for fixed ’s
2. Compute downlink beamformer as a function of UL solution
3. Update ’s via projected subgradient ascent where subgradient for is
Convergence is shown both theoretically and numerically
Contribution #2: Coordinated Per-Antenna Maximum Power Minimization for Low-Resolution Systems
Notes: We first formulate the maximum transmit power minimization problem for downlink which is our primal problem. Here, we need to satisfy a target SQINR (signal to quantization and interference plus noise ratio). This expression gives the transmit power of m-th BS antenna. Each power is upper bounded by p0, and our final target is to minimize p0 by desinging beamformer w. As you can see here, the SINR expressions are coupled with quantization error.
Here on the righthand side, we have a virtual uplink problem. It looks complicated, but it consists of the inner part and outer part. The inner part is the minimization of the total transmit power for a given target SINR. The outer part is maximization over D_i which is the noise covariance matrix at BS_i.
At this point, they are two separate problems.

## Slide 14: Simulation Results of the Proposed Q-CoMP and Q-CoMP-PA
Peak power vs. target SQINR
16 antennas, 4 cells, 2 users per cell, 32 subcarriers
Saturation points [Vasjanov et al.]
[1] A. Vasjanov and V. Barzdenas, “A Review of Advanced CMOS RF Power Amplifier Architecture Trends for Low Power 5g Wireless Networks”, Electronics, vol. 7, no. 11, 2018
Contribution #2: Coordinated Per-Antenna Maximum Power Minimization for Low-Resolution Systems
CDF of antenna powers
Peak power
Dynamic range
4 cells (), 32 antennas (), 2 users per cell, 64 subcarriers, ,
32 antennas, 3 cells, 2 users per
cell, 64 subcarriers,
~2 dB reduction over Q-CoMP
~5 dB reduction over Q-Percell
Peak-to-average power ratio
Notes: Let’s move onto the simulation results.
we plot target SINR versus total transmit power, and b means the number of quantization bits
We compare our algorithm against a per-cell approach. Red line are our algorithm and blue line are the per-cell approach.
With 16 antennas, the per-cell approach easily diverges in low-SINR target, however our method diverges in medium SINR.
With 128 antennas which is considered as massive MIMO, our method shows divergence only with 2 bits case.
This figure validates the strong duality between UL and DL. We first plot the uplink cases with red lines, and we placed the downlink results with blue markers. Since they are matching together, we can observe the strong duality from this figure,
For the wideband case, we have 16 antennas, 2 cells, 2 users per cell, and 64 subcarriers. We observed the same trend as narrowband case. The total transmit power increases as resolution decreases, but not very much.

## Slide 15: Summary
Minimize maximum transmit power with target SINR
Impairments: Thermal noise; intra-cell, and inter-cell interference
Quantization noise from low-res ADCs and DACs in base stations
Add per-antenna power constraint to place less burden on power amplifiers and electronics
Objective
  Coordinate multiple base stations
  Design precoding and power control for downlink/uplink
Approach
Use strong duality
Iterative algorithms based on dual space
Update covariance matrix via downlink solution using projected subgradient ascend
Contribution #2: Coordinated Per-Antenna Maximum Power Minimization for Low-Resolution Systems
A
Low-Res
ADC/DAC
Notes: PADC : Power [Watts] = energy/unit time (Joules / sec)
Gersho, Allen, and Robert M. Gray. Vector quantization and signal compression. Vol. 159. Springer Science & Business Media, 2012.

## Slide 16: Learning-Based ML Detection for Massive MIMO Systems with One-bit ADCs
Contribution #3
Contribution #3: Learning-Based ML Detection for Massive MIMO Systems with One-bit ADCs
[1] Yunseong Cho, Jinseok Choi, and Brian L. Evans, “Adaptive Learning-Based Maximum Likelihood and Channel-Coded Detection for Massive MIMO Systems with One-Bit ADCs”, submitted to IEEE Transactions on Vehicular Technologies 2023
[2] Jinseok Choi, Yunseong Cho, and Brian L. Evans, “Robust Learning-Based ML Detection for Massive MIMO Systems with One-Bit Quantized Signals”, IEEE Global Communications, Dec. 2019.

## Slide 17: Background
Problem: Maximum likelihood (ML) detection
  Reduce power consumption by using one-bit I-Q ADCs
  True likelihood function requires *CSI
  Inaccurate channel estimation with one-bit observations
Likelihood probability estimation without CSI
  Count number of received +1 and –1 occurrences
  With high SNR, likelihood function is biased to 0 or 1
  Zero probability wipes out all other likelihood functions
Base Station (BS) Solution
  Add artificial dithering noise with known variance
  Adapt dithering power and estimate SNR for de-noising
Proposed receiver architecture
BS is equipped with antennas and one-bit I-Q ADCs
users w/ single antenna, -QAM vectors
Contribution #3: Learning-Based ML Detection for Massive MIMO Systems with One-bit ADCs
*CSI: Channel State Information
Notes: PADC : Power [Watts] = energy/unit time (Joules / sec)
Gersho, Allen, and Robert M. Gray. Vector quantization and signal compression. Vol. 159. Springer Science & Business Media, 2012.

## Slide 18: One-bit ML detection
 | 1 | 2 |  | 
1 |  |  |  | 
2 |  |  |  | 
 | 1 | 2 |  | 
1 |  |  |  | 
2 |  |  |  | 
One-bit maximum likelihood detection
 | 1 | 2 |  | 
1 | 0.98 0.02 | 0.95 0.05 |  | 0.02 0.98
2 | 0.03 0.97 | 0.71 0.29 |  | 0.82 0.18
 | 0.01 0.99 | 0.13 0.87 |  | 0.07 0.93
 | 1 | 2 |  | 
1 | 0.98 0.02 | 0.95 0.05 |  | 0.02 0.98
2 | 0.03 0.97 | 0.71 0.29 |  | 0.82 0.18
 | 0.01 0.99 | 0.13 0.87 |  | 0.07 0.93
 | 1 | 2 |  | 
1 | 1.0 0.0 | 1.0 0.0 |  | 0.0 1.0
2 | 0.0 1.0 | 0.7 0.3 |  | 0.8 0.2
 | 0.0 1.0 | 0.1 0.9 |  | 0.0 1.0
 | 1 | 2 |  | 
1 | 1.0 0.0 | 1.0 0.0 |  | 0.0 1.0
2 | 0.0 1.0 | 0.7 0.3 |  | 0.8 0.2
 | 0.0 1.0 | 0.1 0.9 |  | 0.0 1.0
Full CSI
Learning-based
Contribution #3: Learning-Based ML Detection for Massive MIMO Systems with One-bit ADCs
Notes: PADC : Power [Watts] = energy/unit time (Joules / sec)
Gersho, Allen, and Robert M. Gray. Vector quantization and signal compression. Vol. 159. Springer Science & Business Media, 2012.

## Slide 19: Dither-and-Learn
Dithered and quantized signal
Much less likely to have zero probabilities
Learning stage (training)
Count # of +1 and -1 based on dithered signals
Estimate the likelihood probabilities
De-noising stage
Use SNR estimates and dithering noise
Update the likelihood probabilities
known to BS
dithering power at th antenna
Contribution #3: Learning-Based ML Detection for Massive MIMO Systems with One-bit ADCs
Notes: PADC : Power [Watts] = energy/unit time (Joules / sec)
Gersho, Allen, and Robert M. Gray. Vector quantization and signal compression. Vol. 159. Springer Science & Business Media, 2012.

## Slide 20: SNR Learning
Data collection
Equivalently thermal noise variance
Offline training measures average number of zeros
BS obtains data set of
SNR learning
Mapping
Supervised learning
Provides estimated value of
Contribution #3: Learning-Based ML Detection for Massive MIMO Systems with One-bit ADCs
Notes: PADC : Power [Watts] = energy/unit time (Joules / sec)
Gersho, Allen, and Robert M. Gray. Vector quantization and signal compression. Vol. 159. Springer Science & Business Media, 2012.

## Slide 21: Dither Power Update
Dithering power is hyperparameter
-step incremental dither-and-learning (iDL)
Divide each training block into sub-blocks
Set if BS does not find change in sign at th sub-block
Set If BS does find change in sign at th sub-block
BS updates dithering power at the th antenna as
The BS has to find suitable dithering power based on the behavior of observations
Contribution #3: Learning-Based ML Detection for Massive MIMO Systems with One-bit ADCs
Notes:   Low dithering power still triggers lots of zero-valued likelihood probabilities
  High dithering power makes noise dominant

## Slide 22: Simulation Results
Symbol Error Rate vs. Transmit Power
Contribution #3: Learning-Based ML Detection for Massive MIMO Systems with One-bit ADCs
32 antennas, 4 users per cell, 45 pilots 4-QAM
64 antennas, 3 users per cell, 45 pilots 16-QAM
Notes: inf resolution

## Slide 23: Soft-Metric for Coded Systems
Log-Likelihood Ratio
  So far, was used for joint detection of the collection of symbols from users
  However, is defined for each single binary bit of user to enable coded systems
Subgroup of symbol vectors
whose th bit of th user is 0
Subgroup of symbol vectors
whose th bit of th user is 1
Frame Error Rate vs. Transmit Power
32 BS antennas, 4 users, 4-QAM, , Rayleigh fading
(Channel Coding) Rate-1/2 Polar code
Contribution #3: Learning-Based ML Detection for Massive MIMO Systems with One-bit ADCs
Notes: Focusing on a single binary bit of one particular user, this is the collection of symbol vector whose corresponding binary information is 0. The other subgroup is defined for binary bit 1

## Slide 24: Summary
Learning-based Data Detection with One-bit ADCs
In high SNR, one-bit observations produce same output
Inaccurate channel estimation with one-bit observations
Objective
  Avoid zero-valued likelihood probability
  Acceptable amount of training
Approach
  Add artificial randomness (dithering) to capture sign changes
  Remove added dithering noise via de-noising stage
  Use deep neural network to estimate SNR
Contribution #3: Learning-Based ML Detection for Massive MIMO Systems with One-bit ADCs
Adaptive dithering noise
Notes: PADC : Power [Watts] = energy/unit time (Joules / sec)
Gersho, Allen, and Robert M. Gray. Vector quantization and signal compression. Vol. 159. Springer Science & Business Media, 2012.

## Slide 25: Joint Hybrid Beamforming and Power Control Using Deep Reinforcement Learning
Contribution #4
[1] Yunseong Cho, C. Dick, and Brian L. Evans, “Fully Autonomous Hybrid Beamforming for mmWave Massive MIMO Systems Using Deep Reinforcement Learning”, to be submitted to IEEE Access
Contribution #4: Joint Hybrid Beamforming and Power Control Using Deep Reinforcement Learning

## Slide 26: Background
Problem
  Deployment of hybrid analog-digital beamforming architecture to scale down # of RF chains.
  Analog components introduce non-convexity and non-linearity
Objective
  Joint optimization of digital and analog components
    High-dimensional analog beamformer: Manipulation of directional propagation
    Low-dimensional digital beamformer: Baseband processing
  Power control
Approach
  Uses reinforcement learning, a goal-oriented approach
  Interaction b/w agent and environment updates neural net parameters
    Take an action at given state and receive instantaneous reward
    Critic : Approximate the sum of discounted rewards through using rewards from training
    Actor : Find the best policy that can maximize
Contribution #4: Joint Hybrid Beamforming and Power Control Using Deep Reinforcement Learning
Notes: PADC : Power [Watts] = energy/unit time (Joules / sec)
Gersho, Allen, and Robert M. Gray. Vector quantization and signal compression. Vol. 159. Springer Science & Business Media, 2012.

## Slide 27: Problem Formulation
System Model: Multicell Multiuser uplink MIMO system
Not a convex problem
because of unit-modular constraints of
: # of Base stations
: # of receive antennas
: # of possible phase angles
Contribution #4: Joint Hybrid Beamforming and Power Control Using Deep Reinforcement Learning
: # of UEs per cell
: # of RF chains
is continuous yet complex matrix
satisfies unit-modulus and discreteness constraints
has max. and min. range
Notes: collection of N elements equally spaced along a straight line

## Slide 28: RL Setup & Deep Deterministic Policy Gradient (DDPG)
Environment
Actor
SINR
Normalize
Vector-wise
Soft-argmax
Slice & Assembly
Critic
Target Critic
Target Actor
Contribution #4: Joint Hybrid Beamforming and Power Control Using Deep Reinforcement Learning
where
Action : agent’s decision
: soft argmax
1
9
0.1
1
9
0.1
0
1
0
0
1
0
0
1
0
1
State : current situation
Reward : feedback from environment
All SINRs satisfy target
At least one SINR satisfies target
All SINRs improve
Power penalty
1. Update to minimize
2. Update to maximize
3. Update
DRL Agent: Actor + Critic

## Slide 29: Simulation Results
32 BS antennas, 3 RF chains, 2 cells, 2 users per cell, 2 propagation path
Settings
Result for target SINR
2 dB target SINR for all UEs
After 700+ iterations, all UEs stably satisfy the target SINR
MindtPy solver for mixed-integer nonlinear programs did not produce a meaningful result.
Target SINR
Contribution #4: Joint Hybrid Beamforming and Power Control Using Deep Reinforcement Learning
Notes: N

## Slide 30: Summary
Multi-cell & multi-user hybrid analog-digital architecture
Non-convex constraints and high-dimensional decision variables
Analog beamformers introduce non-convexity and non-linearity
Inter-cell interference needs to be considered in problem formulation
Objective
  High-dimensional analog beamformer on each base station
  Low-dimensional digital beamformer on each base station
  Transmit power for each user
Approach
Actor-critic DRL (DDPG)
Take neural output and apply piece-wise activation function
Contribution #4: Joint Hybrid Beamforming and Power Control Using Deep Reinforcement Learning
&
&
DRL
Notes: PADC : Power [Watts] = energy/unit time (Joules / sec)
Gersho, Allen, and Robert M. Gray. Vector quantization and signal compression. Vol. 159. Springer Science & Business Media, 2012.

## Slide 31: Dissertation Summary
Power-Efficient and Intelligent Wireless Communication Systems
Contribution #1
Contribution #2
Contribution #3
Contribution #4
Adaptive dithering noise
&
&
DRL
A
Low-Res
ADC/DAC
A
Low-Res
ADC/DAC
Notes: PADC : Power [Watts] = energy/unit time (Joules / sec)
Gersho, Allen, and Robert M. Gray. Vector quantization and signal compression. Vol. 159. Springer Science & Business Media, 2012.

## Slide 32: Future Work
Multicell coordination taking channel estimation error into account
Adaptively changing the decision threshold of one-bit ADCs
Spectral efficiency maximization via DRL-based reconfigurable intelligent surfaces
Notes: PADC : Power [Watts] = energy/unit time (Joules / sec)
Gersho, Allen, and Robert M. Gray. Vector quantization and signal compression. Vol. 159. Springer Science & Business Media, 2012.

## Slide 33
Thank you!
Q&A