## Slide 1
DHRUV ANJARIA, KRISHNAJA KODALI
ECE 382N ADV EMBEDDED MICROCONTROLLER SYSTEM
ACCELERATING Convolution FOR IMAGE CLASSIFICATION

## Slide 2: PROBLEM STATEMENT
Convolution
Max Pooling
Max-Pooling-2
Convolution-2
Convolution-3
Flatten
Dense
Dense1
Image Classification using CNN
32x32 input image
30x30 output
The first convolution layer needs to be accelerated

## Slide 3: OVERALL DESIGN
Representation: 16-bit fixed point (12-bit precision)
Verilog
AXI BURST MASTER to transfer data from ocm to dfsm
dfsm manages the flow of data to convolver unit
Convolution for one Kernel (weights hardcoded)
Input to the convolver is 16-bit data
Application module:
Input image is read and written to OCM
Output Index is varied in the application code
Output is written back to an output file
Set PL Frequency to 50MHz
Convolution end interrupt is detected, and timer value is stored
Register to select the index of output to display
OCM
Burst Master
dfsm
Convolver
Slave Registers
Slave
128 bits
128 bits
16 bits
16*30 bits

## Slide 4
BLOCK DIAGRAM

## Slide 5: CONVOLVER
Matmul w0
Matmul w3
Matmul w6
Matmul w1
Matmul1 w4
Matmul w7
Matmul w2
Matmul w5
Matmul w8
….
Shift register
Output store register
Input [15:0]
Output [30*16-1:0]
conv [15:0]
End
Valid

## Slide 6: RESULTS - WAVEFORMS
Design Vision Simulation
FPGA Registers

## Slide 7: RESULTS - ACCURACY
We compared the expected output from SW to our outputs
Below results are for Fixed point representation (4,12)
The average loss in accuracy is 1.77 * 1/(2^12) = 0.0026

## Slide 8: SPEED UP
No of cycles = 3720
PL Frequency = 50MHz
Convolution time:
=3720*(1/50)us
=74.4us
Hardware
Software
Time = 112923
Acceleration
Speedup:
= 112923/74.4
= 1517
% decrease in
Latency = 99.93%

## Slide 9
Debugging Efficiency spent debugging Verilog, when PL clock frequency was the issue.
Flexibility Enhancement: Could have provisioned for different weights, stride and fixed-point representations
Streamlined Model Selection: Wasted Time in model selection.
Optimized Input Size: should have started with smaller inputs to optimize resource allocation and free up space for logic
REGRETS 

## Slide 10: THANK YOU QUESTIONS?