## Slide 1: Numerical ODE Accelerator ECE382N Final Project
By Anthony Hermez and Francisco Fabregat

## Slide 2: Problem
Accelerator to solve differential equations and simulate dynamical systems in High Performance Computing
Applications in:
  Protein interactions
  Physics simulations
  Mathematical modeling
Attempt to make a design that would work for any system of differential equations and then have user application input a system
  (foreshadowing to us being delusional)

## Slide 3: Project Overview
The accelerator solves differential equations applied to particle movement
Chose an algorithm to improve simulation accuracy over longer time periods
Currently simulates movement of one particle
Simulated movement rendered through terminal window

## Slide 4: Verilog Overview
Used FP IP provided by Xilinx
IP uses AXI Stream protocol
Designed to minimize DSP Slice usage per diff. eq. Solver
Had to tailor to participle application

## Slide 5: Optimizations
Fast Inverse Sqrt Algorithm
Pipelined resources
Custom Logic

## Slide 6: User Application Overview
Application generates random initial states for the particle
  Random initial x, y, z position
  Random initial x, y, z velocity
Application reads output from accelerator at 30Hz and renders it on the terminal, showing the particle movement
To display Z axis movement
  * signifies moving away from screen
  ~ signifies moving toward screen

## Slide 7: Results - Overall
The verilog is written specifically for the particle motion simulator, so each different dynamical system would require different Verilog
  Not very portable to other systems
Initially planned to do 40 particles
  Took way too many LUTs
  Stepped the number down to 15 particles
  Ended up with 1 particle because of the complexity and time
Why generate random initial conditions instead of letting the user define?
  Did not want to have user manually enter 6 initial values for all 40 parameters, so making it random made the program run easier

## Slide 8: Results - Verilog
14 DSP Slices per solver (originally 45)
Found workarounds to minimize LUT usage
600x faster (theoretically) than software solution (for a single particle)

## Slide 9: Results - User Application
Initial plan was to host a web server on the Ultra96 board that read the output from the accelerator to have better rendering capability
  FPGA -> Memory -> User Application -> Server
  Not a very practical solution
  Probably doable, but very unnecessary for the scope of the project
Data refresh rate determined by how fast the terminal could be refreshed
  Anywhere between 15 to 33 Hz would render properly
Made parameters in the application such as particle numbers, minimum and maximum values, etc. with a #define, which made changes to the project much easier

## Slide 10: Things to do Different
Don’t start with very ambitious goals
  You will waste time on unnecessary parts of the project
  Start with a working solution and go from there
  I.e. Don’t be delusional
Find a better way to display the z axis movement
Find a way to make this work with any dynamical system or system of differential equations
  While still minimizing DSP usage
Take proper measurements
Start earlier