## Slide 1
LOW POWER DESIGN OF AMBER25 SoC
EE382M – VLSI2 Project Review
  TEAM 4: Instructor:
  Anisa Qazi Prof. Mark McDermott
  Gayatri Sivaraman
  Neena Hulkoti
  Sharukh Shaikh
  Sruthi Somarouthu

## Slide 2: Outline
Design flow
Amber25 architecture
Synthesis Results
Physical Design flow
ECO & Timing Analysis
Power Analysis
Formality results
Challenges faced
What will we do differently?
Key Learnings

## Slide 3: Work distribution
TASK | Owner
Synthesis | Sharukh, Sruthi
Floorplan | Anisa, Sruthi
Powerplan | Neena, Gayatri
PNR, ECO, PT | Sharukh, Neena
PTPX, Formality | Anisa, Gayatri

## Slide 4: Design Targets
TARGETS | REQUIRED
Cycle time | 8 ns
Total Power | 15 mW
Die Area | 0.7
Utilization | 85%
TARGETS | REQUIRED
Cycle time | 8 ns
Total Power | 15 mW
Die Area | 
Utilization | 85%

## Slide 5: Design Flow chart

## Slide 6: SoC Architecture

## Slide 7: Amber25 Architecture
Amber25 is 5 stage pipeline
  Fetch
  Decode
  Execute
  Memory
  Writeback
Separate Data cache and Instruction cache and a register bank with 27 register
32 bit Wishbone bus interface
ALU, Barrel Shifter, Multiplier
Peripherals used: UART, timer and Ethernet MAC

## Slide 8: Synthesis Switches
Topographical mode: Uses feedback from ICC (pin placement and other information) to provide more margin in timing.
‘set DO_TOPO true’
Avoid usage of LVT/RVT cells:
‘set_dont_use [get_lib_cells *LVT*]’
Leakage power optimization:
‘set DO_LEAKAGE_OPT true’
Clock gating:
‘set DO_CLOCK_GATING false’

## Slide 9: Synthesis Results
Area analysis: After obtaining the area from synthesis, overhead has to be added to account for Routing, Power plan and ECO fixes. Hence, typically a margin of 20% is used.
Cell Area (synthesis) | Expected Area (post ECO) | Achieved Area (post ECO)
0.559365 | 0.671238 | 0.639305
0.559365 | 0.671238 | 0.639305
Chart: Expected vs Actual Area Usage
| Margin | Area (post ECO)
 | 0.047573 | 0.95243

## Slide 10: Synthesis Results
Vth Group split:
Critical path Slack:
Zero Setup/Hold Violations
Vth Group Name | Synthesis | Post ECO
HVT | 99.93 % | 99.69 %
RVT | 0.07 % | 0.18 %
LVT | 0 % | 0.13 %
# Total cells | 28400 | 29068
Clock | Period (ns) | Critical path slack (ns)
sys_clk | 8 | 0.0029
sys_slow_clk | 32 | 2.34
mrx_clk | 40 | 4.16
mtx_clk | 40 | 2.94

## Slide 11: Critical Path in Synthesis

## Slide 12: Effect of Clock Gating switch in Synthesis
Power comparison:
Synthesis was performed with and without the switch ‘DO_CLOCK_GATING’
After first round of ICC, the total power increased for the synth db with ‘DO_CLK_GATING’ set as true.
DO_CLOCK_GATING | Total power mW)
FALSE | 5.93
TRUE | 5.999

## Slide 13: Physical Design Flow

## Slide 14: Hard Macros
Instruction and data cache are part of the Amber core
Ethernet SRAM block is a part of the Ethernet MAC
Boot Memory is accessed by Amber25 core via the wishbone.
Metal Layers used: M1-M5
SRAM MACRO | # BLOCKS
Instruction Cache | 4
Data Cache | 4
Boot Memory | 8
Ethernet | 1

## Slide 15: Floorplans
Floorplan rectangular
Floorplan T
Floorplan L
- Area met
- Utilization target almost met
- Routing congestion
- Less flexibility in area reduction
- Fixed x and y
- No flexibility in area reduction
- Low Utilization
- Difficulties with power planning
- Least area
- Maximum utilization
- Less routing congestion
- Better power planning

## Slide 16: Comparison of all Floorplans (before ECO)
QoR | Floorplan Rect. | Floorplan T | Floorplan L
Internal Power(mW) | 5.4 | 5.6 | 4.14
Switch Power(mW) | 1.5 | 1.9 | 1.019
Leakage power(mW) | 6.9 | 8.5 | 0.771
Total Power(mW) | 13.8 | 16.1 | 5.93
Area ( | 0.66187 | 0.6378 | 0.636918
Utilization | 54% | 83.06% | 87.0%
Max IR drop VDD(mV) | 71.3 | 49.58 | 44.12
Max IR drop VSS(mV) | 68.7 | 49.14 | 47.75
QoR | Floorplan Rect. | Floorplan T | Floorplan L
Internal Power(mW) | 5.4 | 5.6 | 4.14
Switch Power(mW) | 1.5 | 1.9 | 1.019
Leakage power(mW) | 6.9 | 8.5 | 0.771
Total Power(mW) | 13.8 | 16.1 | 5.93
 | 0.66187 | 0.6378 | 0.636918
Utilization | 54% | 83.06% | 87.0%
Max IR drop VDD(mV) | 71.3 | 49.58 | 44.12
Max IR drop VSS(mV) | 68.7 | 49.14 | 47.75

## Slide 17: FLOORPLAN L
Instruction Cache
Data Cache
Boot memory
Ethernet
Notes: Why hard blockage?

## Slide 18: Pin Distribution
Ethernet

## Slide 19: Power Rings
M7
Width: 2um
Spacing: 1um
M8
Width: 2um
Spacing: 1um
Notes: Explain we used M1-M5, route power in M6

## Slide 20: Power Grid
M1
Width: 0.12u
Step: 2*1.672
**(M1 pitch = height of standard cell)
M6
Width: 0.112u
Step: 130um
M9
Width: 1u
Step : 130um

## Slide 21: Virtual Pad Placement & IR Drop
IR drop: 44.11 mV (VDD)
47.74 mV (VSS)
4 pairs of {VDD VSS} virtual pads.
Distribute VDD and VSS virtual pads uniformly for lesser IR drop.

## Slide 22
SoC
Placement (Hierarchy)

## Slide 23
Amber Core

## Slide 24
Fetch
Decode
Execute
Amber Core Hierarchy

## Slide 25
Mem
Writeback
Wishbone
Co-processor
Notes: Co-processor is instantiated in amber core and it has 15 registers and control signals. There are dedicated instructions of type coretrans (mrc and mcr) to move the register data from co-processor to amber register bank.
Mrc- co-processor to amber register bank
Mcr- amber register bank to co-processor

## Slide 26
Ethernet
Uart0, Uart1
Misc. Blocks
Boot Memory

## Slide 27: Clock Trees
mrx
mtx

## Slide 28: Clock Trees
sys_clk
sys_clk_slow

## Slide 29
sys_clk
sys_clk_slow
Clock Buffers

## Slide 30: Routing Congestion
Notes: Routing Congestion is ratio of

## Slide 31: Cell density Comparison
Utilization: 54%
Utilization: 83.06%
Utilization: 87%

## Slide 32: Results: Before ECO
Specification | Floorplan L (before eco)
Total Power(mW) | 5.93
Area() | 0.636918
Utilization | 87.0%
Max IR drop VDD(mV) | 44.12
Max IR drop VSS(mV) | 47.75
# Setup Violations | 2
# Hold Violations | 2587
Specification | Floorplan L (before eco)
Total Power(mW) | 5.93
 | 0.636918
Utilization | 87.0%
Max IR drop VDD(mV) | 44.12
Max IR drop VSS(mV) | 47.75
# Setup Violations | 2
# Hold Violations | 2587

## Slide 33: ECO FLOW

## Slide 34: PT Multi-corner Timing Analysis

## Slide 35: Multi-Corner Timing Analysis
Corner | Setup Slack (ns) | Hold Slack (ns)
ss0p95n40c | 0.07 | 0.04
tt1p05v25c | 3.373 | 0.013
ff1p16v125c | 5.39 | 0.001
Chart: 
| ss0p95n40c | tt1p05v25c | ff1p16v125c
Setup Slack (ns) | 0.07 | 3.373 | 5.39

## Slide 36: Critical paths (post ECO)
Decode Register -> Register Bank -> Barrel Shifter -> ALU -> Status Bit Update

## Slide 37
Decode Register -> Register Bank -> Barrel Shifter -> ALU -> Status Bit Update

## Slide 38
MULTICYCLE PATH

## Slide 39
Amber Wishbone -> Wishbone Arbiter -> Amber Wishbone -> Mem D-Cache -> Amber Wishbone -> Execute Register Bank Clock Gate EN

## Slide 40: Post ECO Reports

## Slide 41: Results: Before and After ECO
Specification | Floorplan L (before eco) | Floorplan L (after eco)
Internal Power(mW) | 4.14 | 4.14
Switch Power(mW) | 1.019 | 1.013
Leakage power(mW) | 0.771 | 1.057
Total Power(mW) | 5.93 | 6.210
Area() | 0.636918 | 0.639305
Utilization | 87.0% | 89.07%
Max IR drop VDD(mV) | 44.12 | 44.20
Max IR drop VSS(mV) | 47.75 | 47.87
Specification | Floorplan L (before eco) | Floorplan L (after eco)
Internal Power(mW) | 4.14 | 4.14
Switch Power(mW) | 1.019 | 1.013
Leakage power(mW) | 0.771 | 1.057
Total Power(mW) | 5.93 | 6.210
 | 0.636918 | 0.639305
Utilization | 87.0% | 89.07%
Max IR drop VDD(mV) | 44.12 | 44.20
Max IR drop VSS(mV) | 47.75 | 47.87

## Slide 42: PTPX Power Analysis flows
Leakage power estimation gives fairly accurate results
There exists 3 different methodologies for estimating active power
Static activity factor (AF) propagation:
Obtain approximate AF for each block. Propagate the same inside the block
Estimate power based on this
Key points:
  Inaccurate
Forced gate GLS:
Run RTL simulation and obtain values of key nodes
Run GLS by forcing the values on those mapped(RTL->Gate level) nodes and obtain VCD dump
Convert VCD to SAIF
Use this SAIF to estimate power
Key points:
  Faster compared to Full GLS
  Accurate AFs for all nodes
Full GLS:
Run gate level simulation of average use case to get a VCD dump
Convert VCD to SAIF
Use this SAIF to estimate power
Key points:
  Need a working timing GLS simulation framework – tedious, runs take time
  Accurate AFs for all nodes
*GLS: Gate level simulation
*VCD: Value change dump
*SAIF: Switching activity interface format
Reference: SNUG Boston 2010 (Measuring active power using PTPX: A User perspective)
Notes: Simple summations of the total device width or the total device width attached to power and ground supplies can be used to calculate reasonable leakage approximations. Leakage power is not nearly as pattern dependent as active power.
We referred to the paper from SNUG mentioned below to understand the flow for power estimation
Leakage power is not dependent on the block activities, thus most of the devices gives almost accurate results.
But, active power depends on activity factors and our power estimates depend on the accuracy of these. According to this paper, there are 3 methodologies that are usually followed.

## Slide 43: Steps to obtain activity factor
Run GLS and obtain VCD
Convert VCD to SAIF: “vcd2saif –input gls_dump.vcd –o gls_dump.saif”
Read SAIF in ptpx: “read_saif –input gls_dump.saif –strip_path tb/dut/u1”
Can report the activity factors: “report_switching_activity”

## Slide 44: Power report (Static AF propagation)

## Slide 45: Formality Flow

## Slide 46: Formality check: RTL vs DC Netlist
No failing points
No abort points
1 Unmatched point in REF design due to logic removal in optimization
285 unmatched points in IMP design due to clock gating latch insertion during synthesis
Test Passed!

## Slide 47: Formality check: DC vs ICC post ECO Netlist
No failing points
No abort points
No unmatched points
Test passed!

## Slide 48: Final Results: Post ECO
QoR | Specification | Results | Margin
Cycle time (ns) | 8 | 8 | 0
Total power (mW) | 15 | 6.210 | 58.6 %
Area | 0.7 | 0.639305 | 8.67 %
Utilization (%) | 85 | 89.07 | 4.07 %
Max. IR Drop VDD (mV) | <50 | 44.20 | 5.8 mV
Max. IR Drop VSS (mV) | <50 | 47.87 | 2.13 mV
Verify LVS | CLEAN | CLEAN | -
Verify DRC | CLEAN | CLEAN | -
Formality | CLEAN | CLEAN | -
QoR | Specification | Results | Margin
Cycle time (ns) | 8 | 8 | 0
Total power (mW) | 15 | 6.210 | 58.6 %
 | 0.7 | 0.639305 | 8.67 %
Utilization (%) | 85 | 89.07 | 4.07 %
Max. IR Drop VDD (mV) | <50 | 44.20 | 5.8 mV
Max. IR Drop VSS (mV) | <50 | 47.87 | 2.13 mV
Verify LVS | CLEAN | CLEAN | -
Verify DRC | CLEAN | CLEAN | -
Formality | CLEAN | CLEAN | -

## Slide 50: Challenges faced Power Planning
Routing congestion leading to shorts during ECO iterations
Reason: M9 Power strap placed at centre standard cell area

## Slide 51
Unnecessary long routing of sys_clk_slow
Reason: UART blocks were placed far apart
Challenges faced
Clock Tree

## Slide 52
Initial DC & ICC use: HVT + RVT
Initial DC & ICC use: Only HVT
** ECO in both cases uses: HVT, RVT & LVT
Challenges faced
Setup Slack (post ECO, ss corner)

## Slide 53: Challenges faced Routing Congestion
In ECO iterations, verify_lvs reported several shorts
Reason: Utilization was around 91%, routing congestion was high
Solution: Went back and increased the standard cell region area of floorplan

## Slide 54: Challenges faced Hold Time Fixing
ECO was unable to fix a hold violation even with multiple iterations
Reason: Hold violations on ‘brd_rst’
‘brd_rst’ is an asynchronous reset
**Hierarchy: system -> clocks_resets -> eth_top
**‘brd_rst’ signal is passed as ‘wb_rst_i’ to ‘eth_top’
Set as false path in constraints
set_false_path –from [get_ports brd_rst]

## Slide 55: What would we do differently?
Adapt a better power estimation technique by extracting activity factors from GLS VCD.
Reference: VLSI2 – Lecture notes
(Early Design Planning – Front End)

## Slide 56: What would we do differently?
Follow CPF/UPF based flow and implement voltage domains for blocks based on their specifications.

## Slide 57: Key Learnings
Clock Gating can decrease dynamic power, but may increase leakage power which might lead to increase in total power
Utilization can be increased by reducing area or increasing blockage
Power straps should be spaced optimally considering IR drop and routing congestion
Increase width of power straps for reducing IR drop.
Virtual pads must be equidistant to have uniform IR drop
Extra area has to be accounted for in order to fix violations during ECO iterations
Proper database management and good communication between team members helps complete the project smoothly

## Slide 58: Questions?

## Slide 59: Backup

## Slide 60: IR Drop comparison
IR drop: 49.86 mV (VDD)
48.96 mV (VSS)
IR drop: 44.11 mV (VDD)
47.74 mV (VSS)

## Slide 61: DC area report

## Slide 62: DC timing report

## Slide 63: ICC area report: Post ECO

## Slide 64: ICC Utilization report: Post ECO

## Slide 65: PTPX results