## Slide 1: Computer Architecture: Fundamentals, Tradeoffs, Challenges Chapter 2: The ISA
Yale Patt
The University of Texas at Austin
Austin, Texas
Spring, 2025

## Slide 2: Outline
The ISA -- What is it?
  The interface between hardware and software
  A specification
  NOT microarchitecture
  NOT just the instruction set
The Instruction
  The atomic unit of processing
  Changes the state of the machine
Characteristics of an ISA (using LC-3b as an example)
The LC-3b instruction set
Other ISAs
  X86
  RISCV
ISA Tradeoffs (with examples)

## Slide 3: What is the ISA?
A specification
  The interface between hardware and software
A contract
  What the software demands
  What the hardware agrees to deliver

## Slide 4: NOT Microarchitecture
Architecture
  Software Visible
  Address Space, Addressability
  Opcodes, Data Types, Addressing Modes
  Privilege, Priority
  Support for Multiprocessors (e.g., TSET)
  Support for Multiprogramming (e.g., LDCTX)
Microarchitecture
  Not Software Visible
  Caches (although this has changed, …sort of)
  Branch Prediction
  The instruction cycle
  Pipelining
DIGRESSION (nugget): You have a brilliant idea, and
It requires a change to the ISA or to the uarchitecture.

## Slide 5: Another DIGRESSION (nugget)
The pure distinction between ISA vs uarchitecture
  ISA is visible to the software
  Microarchitecture is “underneath the hood”
BUT some have noticed that…
  If you let the compiler know how the ISA is implemented,
  i.e., if you break the walls between the transformation levels,
  You can produce better code for that implementation
  …at the expense of compatibility
Today, with the impending demise of Moore’s Law,
  Computer Architecture is looking for ways to still be relevant
  I have been preaching: Break the layers!
  MIT recent white paper: “There is plenty of room at the top!”

## Slide 6: Characteristics of an ISA (e.g., the LC-3b)
Processor State (memory, registers)
  Memory addressability: byte
  Memory address space: 2^16
  Registers: 8 GPR, Condition Codes N, Z, P
  Word length: 16 bits
  Program Counter (Actually, Instruction pointer)
  Process Status Register (contains Privilege, Priority, CC)
Privilege: 2 levels, supervisor, user
Priority: 8 levels
Instruction format: fixed length, uniform decode. 16 bits
  Flynn’s observation: Two or three lengths better than all the same
Endian-ness: little endian
Instructions (opcode, addressing mode, data type)
  Opcode (14 opcodes, including XOR, SHF, LDB)
  Addressing modes (PC-relative, Register + offset)
  Data types (2’s complement 16 bit integers, bit vector)
  Three-address machine (Load/Store ISA)

## Slide 7: The LC-3b Instruction Set

## Slide 8: Pragmas (aka Pseudo-ops)
Not part of the instruction set
  Not executed by the computer
Messages from the programmer to the translater
  Necessary for the translater to produce object code
  Opportunity for programmer to affect performance (e.g., hints)

## Slide 9: Characteristics of an ISA (continued)
Vector architecture (instructions, operands)
  Not part of the LC-3b
Virtual memory specification: not yet part of LC-3b!
  Address space
  Translation mechanism
  Protection
  Page size
System architecture
  State to deal with: trap vector table, interrupt vector table
  Interrupt, exception handling
  Instructions for the O/S to use (RTI)
NOT the instruction cycle (that is part of the uarch)

## Slide 10: x86
Variable length instruction (one byte to 16 bytes)
Characteristics
  Rich set of addressing modes
  Two-address machine
  SSE extension (originally, MMX)
  Not load/store
  Three page sizes (4KB, 2MB, 1GB)
  Register sizes: 8b, 16b, 32b, 64b, 128b, …
  Example: AH, Ax, EAX, …
  Memory: Byte addressable, 64 bit address space

## Slide 11: RISCV
The 5th chip from Professor David Patterson’s group
  UC Berkeley
  Nothing (really) in common with their other four risc chips
Mostly handled by Professor Krste Asonovic
Major selling point: Open Source
Overall structure
  Multiple subset ISAs (Integer, Float, MUL/DIV, Atomic, etc.)
  Designers build their own system, picking and choosing
  MUST contain one of the Integer subsets (32-bit or 64-bit)
  The rest (extensions) are up to the designer

## Slide 12: RISCV (characteristics)
The subsets
  Integer: 32-bit (RV32I), 64-bit (RV64I), 128-bit (RV128I)
  Float extension: 32-bit (RV32F), 64-bit (RV64D), 128-bit (RV128Q)
  M extension: Integer MUL/DIV
  A extension: Atomic instructions
  L extension: Decimal float
  C extension: Compressed
  B extension: Bit manipulation
  J extension: Dynamically translated
  T extension: Transactional memory
  P extension: Packed SIMD
  V extension: Vector operations
  E extension: Embedded Controller (RV32E)
  G extension: A system, really (IMAFD)

## Slide 13: RISCV Characteristics (continued)
RV32I (32 bit Integer data type)
  47 distinct opcodes (
    loads, stores, shifts, arith, logic, compare, branch, jump, synch, count
  32 GPRs (x0 to x31, x0=0, x1 used for call return linkage)
  Also contains a PC
  32 bit instructions
    Can be extended by a multiple of n bits
    Mixture allows for unaligned access
    Also allows for 16 bit instructions, but then restricted to 8 registers
  4 basic instruction formats
  Other
    Little endian
    Load/Store
    No predication
    Conditional branches use GPRs, not condition codes

## Slide 14: ISA Tradeoffs (examples)
Dynamic-Static Interface (The Semantic Gap)
ISA closer to the HLL
ISA closer to the control signals
ISA-level CAPABILITY (aka “Security”)
  instructions included privilege needed
  Intel 432, IBM System 38, Data General Fountainhead
  All failed! Why? Performance was very slow
PREDICATION
  x86 CMOV, ARM inst[31:28], THUMB IT block
Support for multiple ISAs on the same chip
  ARM T bit, VAX Compatibility mode bit
  Both in the PSR, making it part of the ISA.

## Slide 15: ISA Tradeoffs (continued)
REGISTER SET -- how many reg, how many bits each
  Many machines: 32 32-bit registers
  More registers save spills to memory, but longer context switch
  x86 now has 512-bit registers
  Itanium has 1-bit predicate registers
  Register window (SPARC ISA) vs set of gprs
Condition codes vs gprs. (MIPS, CDC6600 used gprs)
  Serialization of code vs getting something done for nothing
  John Cocke RS6000 -- 8 sets of 4 condition codes each
RICH INSTRUCTION SET vs. LEAN INSTRUCTION SET
  Hewlett-Packard: HPPA RISC had 140 opcodes
  So much for RISC being a small set of instructions!

## Slide 16: ISA Tradeoffs (continued)
Do we include complex instructions (faster, but more gates)
  EDITPC -- for COBOL
  INDEX -- for Fortran
  AOBLEQ -- For loop
  LDCTX/SAVCTX -- to swap in/out context needed for next quantum
  Test and Set (an Atomic operation) – for multiprocessing
  CALL -- formal procedure call
    more work, but cleaner interface to libraries
    In addition to JSR (quick and simple)
  FF -- find first
  INSQUE/REMQUE -- doubly linked list data type
  TRIADS – example: MAC (multiply accumulate)
  CHMD -- to change privilege mode
Notes: Had to remove PROBE since it didn’t fit. Can add it back sorry.

## Slide 17: ISA Tradeoffs (continued)
INST SET Orthogonal vs Tailoring to each opcode
LOAD/STORE vs NOT Load/Store
  Load/Store: Can’t access storage and operate in same instruction
  LC-3b is load/store, x86 is not
  Load/Store had more importance before o-o-o processing
MEMORY ADDRESS SPACE -- keeps getting larger
MEMORY ADDRESSABILITY -- depends on needs
  Most memories: byte addressable (for data processing)
  Scientific machines -- 64 bits
  Burroughs 1700 -- one bit (needed for virtual machines)

## Slide 18: ISA Tradeoffs (continued)
VLIW (compile time) vs. Superscalar (do it at runtime)
  Compile time in ISA, runtime is uarchitecture (Superscalar)
  VLIW: Hard to find enough instructions to fill the long word,
  VLIW is fast because there are no dependencies at runtime.
  Examples Multiflow, cydra five
  Itanium 3 in one VLIW, but allows for dependencies
0,1,2,3 address machines. 3 addresses are needed.
How many have to be explicit?
  0. stack machine: pop, pop, compute, push
  1. one accumulator when reg were expensive AC  AC + Memory
  2. two. X86 (Rd  Rd op Rx)
  3. LD/ST all three are explicit Rd  Rs1 op Rs2 (LC-3b)
  VAX ISA had both 2-address and 3-address

## Slide 19: ISA Tradeoffs (continued)
Word length (max size processed as a unit)
  VAX 32 bits, x86 initially 16 bits, then 32, today 64;
  CRAY-1 64bits
  DEC System 20, an AI Machine. LISP’s car, cdr needed 36 bits
Help for the programmer or help for the microarchitect
  Aligned vs. unaligned accesses easier – who gets the easy job?
  PDP11 NO, VAX YES, ALPHA NO
  Data types; int, float, bitvector, char string, doubly linked list
  Addressing modes; indirect, index, autoinc/autodec/ SIB byte

## Slide 20: ISA Tradeoffs (continued)
PAGE SIZE
  (4KB vs more than one size
  Intel has 3three: 4KBm 2MB, 1GB)
  Faruk has all sizes 2^n for n greater or equal to 12
  Efficient use of TLB, vs. Wasted space
  Better use of TLB (fewer PTEs) vs. wasted space
  Too many PTEs vs longer access time
I/O architecture
  Today most use memory mapped I/O with LD,ST
  OLD days, special I/O instructions
  x86 still has both
Compile time vs run time
  MIPS use of NOPS rather than hardware interlocks

## Slide 21: ISA Tradeoffs (continued)
Synch vs Asynch
Instruction format:
  Most: fixed length, uniform decode (easier multiple decode)
  X86: variable length more work done per instruction)
  Intel 432: different sizes for different opcodes (Nightmare!)
SPEED DEMONS vs. BRAINIACS
  Alpha: Speed demon, 200 MHz;
  Pentium: Brainiac, 66MHz

## Slide 22: Obrigado!!