## Slide 1: Towards Scalable CPU Design
Chester Cai
Feb 2026

## Slide 2: Single Thread Performance Still Matters
Many applications are hard to parallelize
  Compilers, OS, runtime systems
  Interactive Applications
  Many accelerator workloads still need CPU orchestration
CPU vendors continue to push for more performance/better efficiency

## Slide 3: Transistor Scaling is Slowing Down
CPU frequency has not changed much in the past 15 years
Cost of technology scaling is increasing
  Building larger structures is difficult, will only be more difficult
We must rely on more advanced architectural improvements
Chart: Feature Size (nm)
| 2007 | 2011 | 2013 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
AMD | 65 | 32 | 28 | 14 | 7 | 7 | 5 | 4
Intel Core | 32 | 22 | 14 | 10 | 7 | 4 | 3
Intel Atom | 10 | 7 | 4 | 3
Apple | 5
Exynos | 14 | 10 | 10 | 8 | 7 | 5
Qualcomm | 4

## Slide 4: Industry Trends – Wider and Deeper
Chart: Out-of-Order Window Size
| 2007 | 2011 | 2013 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
AMD | 72 | 128 | 128 | 192 | 224 | 256 | 320 | 448
Intel Core | 168 | 192 | 224 | 352 | 512 | 512 | 576
Intel Atom | 208 | 256 | 256 | 416
Apple | 1000
Exynos | 96 | 100 | 228 | 228 | 228 | 256
Qualcomm | 680
Chart: Width Scaling
| 2007 | 2011 | 2013 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
AMD | 3 | 4 | 4 | 6 | 6 | 6 | 6 | 8
Intel Core | 4 | 4 | 4 | 5 | 6 | 6 | 8
Intel Atom | 4 | 5 | 6 | 8
Apple | 8
Exynos | 4 | 4 | 6 | 6 | 6 | 8
Qualcomm | 8

## Slide 5: Outline
Start from a baseline configuration (Intel Golden Cove(2021) with some idealizations), we sweep each configuration at different widths
As we gradually relax different constraints on the processor, we show what would it take to get the performance benefits of scaling
We will talk about how easy/hard to scale each stage, and the potential research opportunities involved

## Slide 6: The Scarab Simulator
Originally an internal HPS simulator developed in 1998
Major upgrade and open sourced in 2019
  Supports 64-bit binary
  Integrated Ramulator
Scarab 2.0 maintained and updated by Heiner Litz from UCSD

## Slide 7: Baseline Parameters
Core | 8-wide issue, 128 entry Fetch Queue 512 entry ROB, 256 entry Reservation Station, 8-wide retire 192 entry Load Queue, 128 entry Store Queue 10 Execution Ports (each supports all operations)
Predictors | 64KB TAGE-SC-L, 8-wide/1 taken per cycle, 8K entry BTB
Caches | 32KB 8-way I-Cache, 1R, 1W (2 banks) 32KB 8-way D-Cache, 4R, 2W 1MB 16-way LLC
Retire width, BP width, Execution Ports scale 1:1 with issue width

## Slide 8: Baseline Width Scaling
Chart: Width
| 8 | 12 | 16 | 20 | 24
Baseline | 2.1479 | 2.2544 | 2.2893 | 2.3047 | 2.3092

## Slide 9: With Perfect BP and D-Cache
Chart: Width
| 8 | 12 | 16 | 20 | 24
Baseline | 2.1479 | 2.2544 | 2.2893 | 2.3047 | 2.3092
Perfect BP | 2.6126 | 2.7772 | 2.8273 | 2.8544 | 2.8665
Perfect DC | 3.2442 | 3.5649 | 3.6738 | 3.7139 | 3.732
Perfect BP+DC | 4.3641 | 5.014 | 5.2541 | 5.3712 | 5.4197

## Slide 10: With More BP Bandwidth (1->3 Takens per Cycle)
Chart: Width
| 8 | 12 | 16 | 20 | 24
Perfect BP+DC | 4.3641 | 5.014 | 5.2541 | 5.3712 | 5.4197
Perfect BP+DC+More BP Bandwidth | 4.8115 | 5.4726 | 5.6196 | 5.6577 | 5.6767

## Slide 11: With More D-Cache Ports (1/2 of the width)
Chart: Width
| 8 | 12 | 16 | 20 | 24
Perfect BP+DC+More BP Bandwidth | 4.8115 | 5.4726 | 5.6196 | 5.6577 | 5.6767
Perfect BP+DC+More BP Bandwidth+More DC Ports | 4.8876 | 5.7134 | 6.0138 | 6.1333 | 6.1974

## Slide 12: With a Bigger ROB(6k entries)
Chart: Width
| 8 | 12 | 16 | 20 | 24
Perfect BP+DC+More BP Bandwidth+More DC Ports+6K ROB | 5.0965 | 6.0565 | 6.426 | 6.5889 | 6.6755
Perfect BP+DC+More BP Bandwidth+More DC Ports | 4.8876 | 5.7134 | 6.0138 | 6.1333 | 6.1974

## Slide 13: Scaling the Rest of the Backend
Chart: Width
| 8 | 12 | 16 | 20 | 24
""+Large RS+Large LSQ | 5.7908 | 7.6326 | 8.7293 | 9.3752 | 9.8541
""+Large LSQ | 5.1883 | 6.3888 | 6.9089 | 7.1785 | 7.33
""+Large RS | 5.2215 | 6.2611 | 6.6807 | 6.8687 | 6.9731
Perfect BP+DC+More BP Bandwidth+More DC Ports+6K ROB | 5.0965 | 6.0565 | 6.426 | 6.5889 | 6.6755

## Slide 14
Chart: Width
| 8 | 12 | 16 | 20 | 24
Baseline | 2.1479 | 2.2544 | 2.2893 | 2.3047 | 2.3092
Perfect DC | 3.2442 | 3.5649 | 3.6738 | 3.7139 | 3.732
Perfect BP+DC | 4.3641 | 5.014 | 5.2541 | 5.3712 | 5.4197
Perfect BP+DC+More BP Bandwidth | 4.8115 | 5.4726 | 5.6196 | 5.6577 | 5.6767
Perfect BP+DC+More BP Bandwidth+More DC Ports | 4.8876 | 5.7134 | 6.0138 | 6.1333 | 6.1974
Perfect BP+DC+More BP Bandwidth+More DC Ports+6K ROB | 5.0965 | 6.0565 | 6.426 | 6.5889 | 6.6755
""+Large RS+Large LSQ | 5.7908 | 7.6326 | 8.7293 | 9.3752 | 9.8541
""+Large LSQ | 5.1883 | 6.3888 | 6.9089 | 7.1785 | 7.33
Baseline
+Perfect DC
+Perfect BP
+More BP Bandwidth
+6K ROB
+Large RS
+Large LSQ
Putting it All Together
+More DC Ports

## Slide 15
Chart: Width
| 8 | 12 | 16 | 20 | 24
-Max RS | 5.1883 | 6.3888 | 6.9089 | 7.1785 | 7.33
-Max LSQ | 5.2215 | 6.2611 | 6.6807 | 6.8687 | 6.9731
-6k ROB | 4.8257 | 5.7061 | 6.0395 | 6.1863 | 6.2618
-Max D-Cache | 5.7117 | 7.1815 | 7.679 | 7.8603 | 7.9393
"-Scaled Frontend" | 4.954 | 6.2688 | 7.0363 | 7.5372 | 7.8355
"-Perfect DC" | 3.72 | 4.2064 | 4.4077 | 4.4976 | 4.5566
"-Perfect BP" | 3.9237 | 4.6783 | 5.0786 | 5.2927 | 5.4215
Baseline Ablation | 5.7908 | 7.6326 | 8.7293 | 9.3752 | 9.8541
With Everything
-More DC Ports
-More BP Bandwidth
-Large RS
-Large LSQ
-6K ROB
-Perfect DC
-Perfect BP
Ablation Study

## Slide 16: What can CPU architects do about them?
Scaling the width of the core involves scaling the bandwidth of every stage of the core, including
  Prediction, Fetch, Decode, Rename, Scheduling, Execution, Memory/Cache Bandwidth, Retire
Most of these stages involve non-linear increase in power/area
I will break the challenges into 2 categories

## Slide 17: Building Big Structures is Hard
Many on-chip structures are highly ported, and/or require fully associative searches, making it very difficult to increase their sizes
  Physical register, LSQ, Reservation Stations, Miss Status Handling Registers(MSHR), ROB
But all of them are necessary to scale the width and depth
Can we come up with better algorithms that utilizes these resource more efficiently?
  Localizing the Tag Comparisons in the Wakeup Logic to Reduce Energy Consumption of the Issue Queue [MICRO’24]
  Virtual Physical Registers[HPCA’98] Speculative Register Reclamation [HPCA’23]
  Criticality Driven Fetch [MICRO’ 21]

## Slide 18: Sequential Algorithms Do Not Scale Well
Many frontend stages performs work that are sequential in nature
  Branch prediction
  x86 Decode
  Rename
  Scheduling
Very hard to increase the width of these stages, often come at non-linear increase in power/area
Can we come up with algorithms that is scaling friendly?
  Intel Atom Clustered Frontend
  Alternate Path Fetch [MICRO 2024]
8-WIDE
4-WIDE
4-WIDE

## Slide 19: Conclusion
The need for CPU performance has not deceased even in the era of specialization and parallelism
CPUs will continue to get wider and deeper to extract more performance
It’s our job as architects to solve the challenges involved in scaling the core

## Slide 20: Questions?

## Slide 21: Baseline Parameters
BP: TAGE-SC-L, 8K entry BTB, single cycle latency, up to the first taken or (width) # of instructions
I-Cache: 32KB, 8-way
ROB: 512 Entries
  256 Reservation Stations, 192 Load Queue, 128 Store Queue
D-Cache: 32KB D-cache, 8 way
  4 read ports, 2 write ports
Functional Unit: (1.2*width) # of FUs that can handle any instruction
Retire width: (width)
Last Level Cache: 1MB, 16-way, 18-cycle latency

## Slide 22
Chart: Per Benchmark
| perlbench_17_s_ref | gcc_17_s_ref | mcf_17_s_ref | omnetpp_17_s_ref | xalancbmk_17_s_ref | x264_17_s_ref | deepsjeng_17_s_ref | leela_17_s_ref | exchange2_17_s_ref | xz_17_s_ref | bwaves_17_s_ref | cactuBSSN_17_s_ref | lbm_17_s_ref | wrf_17_s_ref | cam4_17_s_ref | pop2_17_s_ref | imagick_17_s_ref | nab_17_s_ref | fotonik3d_17_s_ref | roms_17_s_ref | IPC
8_wide_exp_11_exec | 4.5661 | 4.3644 | 6.3667 | 4.6199 | 5.1936 | 6.4142 | 6.1974 | 6.3452 | 6.0206 | 7.1227 | 6.8908 | 4.8487 | 7.5312 | 5.4254 | 5.3171 | 5.9728 | 7.9616 | 5.9637 | 5.6649 | 6.0811 | 5.7908
12_wide_exp_11_exec | 5.2742 | 5.0065 | 8.9455 | 4.6359 | 6.3068 | 8.907 | 8.0642 | 8.6535 | 8.9944 | 10.117 | 10.0483 | 8.6187 | 11.2959 | 7.3875 | 6.5547 | 8.5015 | 8.5516 | 8.086 | 8.1701 | 9.0549 | 7.6326
16_wide_exp_11_exec | 5.6183 | 5.2605 | 10.0373 | 4.6347 | 6.9 | 11.1318 | 8.6695 | 9.2262 | 11.9476 | 12.5946 | 11.6558 | 12.4522 | 15.059 | 8.6708 | 7.1665 | 10.4865 | 8.5739 | 9.5685 | 10.1219 | 11.9928 | 8.7293
20_wide_exp_11_exec | 5.8133 | 5.3729 | 10.4205 | 4.6389 | 7.2817 | 13.0753 | 8.8755 | 9.4561 | 14.8664 | 14.5761 | 11.9368 | 14.0452 | 18.8235 | 9.5088 | 7.5237 | 12.0491 | 8.5859 | 10.1984 | 11.8455 | 14.8372 | 9.3752
24_wide_exp_11_exec | 5.9562 | 5.4459 | 10.5619 | 4.6401 | 7.4522 | 14.7355 | 8.9562 | 9.568 | 17.719 | 16.0036 | 12.0041 | 18.7466 | 22.5857 | 10.0758 | 7.6998 | 13.1339 | 8.5927 | 10.4076 | 13.3993 | 17.3958 | 9.8541

## Slide 23: Practical BP/BTB implementation
TAGE cookbook
  (https://hal.science/hal-04804900v1/document)
BTB organizations
  (https://dl.acm.org/doi/10.1145/3613424.3623774)