## Slide 1: Networking and Network Software Development
EE 422C
Adapted from Dr. Jeffrey Miller, USC and Dr. Nandakumar

## Slide 3: Layers in socket communication

## Slide 4: Network Layers (cont.)
Two Internet hosts are connected via two routers and the corresponding layers used at each hop.
The application on each host executes read and write operations as if the processes were directly connected to each other by some kind of data pipe.
Every other detail of the communication is hidden from each process.
  The underlying mechanisms that transmit data between the host computers are located in the lower protocol layers.

## Slide 5: Transport Layer
Establishes connections between hosts
Enables ordering and delay control of packets
  ensures that packets are ordered properly, and are delivered with specified delay
Enables multiplexing
  uses different ports to distinguish between different applications, much like names on a postal address distinguish between people at the same physical location

## Slide 6: Network Layer
Connectionless
  each packet sent independently, might be through different routes
Host addressing
  Every host in the network must have a unique address that determines where it is.
  This address is normally assigned from a hierarchical system.
    For example, you can be "Fred Murphy" to people in your house, "Fred Murphy, 1 Main Street" to Dubliners, or "Fred Murphy, 1 Main Street, Dublin" to people in Ireland, or "Fred Murphy, 1 Main Street, Dublin, Ireland" to people anywhere in the world.
    On the Internet, addresses are known as Internet Protocol (IP) addresses.

## Slide 7: Packets in the network

## Slide 8: The Internet
Development started at MIT in 1962 and later funded by ARPA, the research office of DOD. (Often called ARPANet.)
  Why the department of defense?
1970’s rapid expansion in academic and commercial communities.
Backbone privatized in mid 90’s.
  Allowed commercial enterprises to make money via the internet
  Did Al Gore invent the internet?

## Slide 9: IP Addresses
An IP address is a unique address that is required of all computers that communicate on a network
IPv4 addresses consist of 32 bits separated as 4 numbers of 8 bits each
› 128.125.253.146
IPv6 addresses consist of 128 bits separated as 8 sets of 4 hexadecimal values
› fe29:392A:3396:829E:5591:40d3:3495:109A
› NOTE that if all four hexadecimal values are 0, the term will be omitted
  fe29:392A:3396::5591:40d3 (4th, 7th, and 8th terms are 0000)

## Slide 10: IPv6 Address Space
How many IPv4 addresses are there?
› 32 bits
= 232 addresses
= 22 * 230 addresses
= ~4 billion addresses
How many IPv6 addresses are there?
› 128 bits
= 2128 addresses
= 28 * 2120 addresses
= 256 * 2120 addresses
210 = 1024 = ~103 = thousand 220 = 1,048,576 = ~106 = million 230 = ~109 = billion
240 = ~1012 = trillion
250 = ~1015 = quadrillion 260 = ~1018 = quintillion
270 = ~1021 = sextillion 280 = ~1024 = septillion 290 = ~1027 = octillion 2100 = ~1030 = nonillion 2110 = ~1033 = decillion 2120 = ~1036 = undecillion

## Slide 11: IPv4 Classes
Network numbers are managed by ICANN
The Internet Assigned Numbers Authority (IANA) was founded by USC/ISI and transferred to ICANN in 1998
› ICANN was founded primarily to take over control of IANA

## Slide 12: IPv4 Special Addresses

## Slide 13: Finding Your IP Address
Open a command line and type ipconfig in Windows ifconfig in Mac or Linux

## Slide 14: Routing
Routing is the process of sending data from one computer to another
Routers use two algorithms – Distance Vector and Link State
› The specifics of those algorithms are outside the scope of this lecture

## Slide 15: Routing
Source
Destination

## Slide 16: Finding a Route
This is a very complicated process, but running tracert (Windows) or traceroute (Mac, Linux) from a command line or terminal will show you all the routers visited from your computer to a destination

## Slide 17: Domain Name System (DNS)
Some servers can be identified by a hostname and domain name
› An example would be www.utexas.edu
› www is the hostname (or an alias for a hostname)
› utexas.edu is the domain name
To find the IP address of a hostname/domain name combination from a command line, run ping or nslookup from a command
line or terminal

## Slide 18: DNS Namespace
The hostname/domain name combination will be mapped to an IP address through DNS servers
› DNS is a hierarchical domain-based naming scheme implemented through a distributed database system for implementing
› DNS was conceived at USC’s ISI and managed there until 1998
› DNS is now managed by ICANN

## Slide 19: DNS Resource Records
Every domain has a set of resource records associated with it, which is what DNS will return based on a certain name
A resource record consists of five items
› Domain Name – the domain of the record
› Time To Live – the higher the value, the more stable the record
› Class – always IN for Internet resources (rarely used outside of that)
› Type – what kind of record it is (see table below)
› Value – the value associated with the record

## Slide 20: Sample DNS Database

## Slide 21: Actual DNS Records

## Slide 22: Ports
Since more than one networked program can run on a computer at the same time, we need a way to uniquely identify them
› Ports allow us to do just that
A client application will specify the port on the server with which to communicate, and that uniquely identifies the server application
A port is in the range from 0 to 65535 (16 bits)
› Ports from 0-1023 (inclusively) are reserved for well-known applications, so root or administrator access is required to run an program on a port in that range
› Ports from 1024-49151 (inclusively) are registered ports and can be used by any application
› Ports from 49152-65535 are dynamic or private ports and are typically used by the operating system when an application needs to pass an application off to a non-registered port

## Slide 23: Well-Known Ports
There are many others, but these are some of the more popular ones
Port | Application
20 | FTP data
21 | FTP control
22 | SSH
23 | Telnet
25 | SMTP
53 | DNS
80 | HTTP
143 | IMAP
443 | HTTPS

## Slide 24: Public and Private IP Addresses
Public IP addresses are able to be seen by any computer in the world and are required for communicating on the Internet
Private IP addresses are typically secured behind a firewall, so explicit access has to be allowed to them
› Private IPv4 addresses are in the following ranges
  Class A Private: 10.0.0.0 – 10.255.255.255
    20=1 network with 224 addresses
  Class B Private: 172.16.0.0 – 172.31.255.255
    24=16 networks with 216 addresses
  Class C Private: 192.168.0.0 – 192.168.255.255
    28=256 networks with 28 hosts on each network
› Private IP addresses must use NAT (see future slide) if accessing the Internet because private IP addresses cannot communicate outside local networks
› If a computer is unable to obtain an IP address, an address in the range 169.254.0.0 – 169.254.255.255 may be assigned
  This IP address is NOT available to the Internet

## Slide 25: NAT
Network Address Translation (or IP Masquerading) allows a computer to have a private IP address
› Private IP addresses are not able to be accessed by hosts outside of the local network
› A NAT server (usually implemented in a router) substitutes its own public IP address in place of the computer’s private IP address
› The NAT server must maintain a NAT table that links the private IP address and TCP/UDP source port combination to the destination IP address
  Since the NAT server’s public IP address has been substituted for the computer’s private IP address in the packet, the response from the destination computer will come back to the NAT server
  The port will let the NAT server know to which computer to forward the response

## Slide 26: NAT Example
20/27

## Slide 27: DHCP
Dynamic Host Control Protocol (DHCP) is used for a computer or router to automatically assign IP addresses and other network configuration (such as the gateway and subnet mask) to computers on the network
› These addresses can be private or public IP addresses
› Most routers assign private IP addresses, such as 192.168.1.101
› Routers often have DHCP servers built into them

## Slide 28: Client- Server
A server is a computer that has at least one program running on it that can service requests from another program
Server hardware is typically more robust than other hardware, but a server can physically be any computer
A client is a computer that requests a service to be performed by another computer
Consider browsing the web. What is the service provided by a web server?

## Slide 29: Servers
Server hardware is typically more robust and expensive than other hardware, but a server can physically be any computer

## Slide 30: Server-Side Programming
It is the program that runs on server dealing with the generation of content of web page. 1) Querying the database 2) Operations over databases 3) Access/Write a file on server. 4) Interact with other servers. 5) Structure web applications. 6) Process user input. For example if user input is a text in search box, run a search algorithm on data stored on server and send the results.
The main programming languages for server-side programming are:
  PHP
  C++
  Java and JSP
  Python
  Ruby on Rails

## Slide 31: Client-Side Programming
Functionality
  Interact with temporary storage
  Make interactive web pages
  Interact with local storage
  Sending request for data to server
  Send request to server
  work as an interface between server and user
The main programming languages (tools) for client-side programming are :
  Javascript
  VBScript
  HTML
  CSS
  AJAX

## Slide 32: “Full Stack” Software Development
A full-stack programmer is a person who is comfortable working with all the technologies required to get an idea to a finished product. This person is familiar with all the layers of software development.
  Server, network, and hosting environment
  Relational and nonrelational databases
  How to interact with APIs and the external world
  User interface and user experience
  Quality assurance
  Security concerns throughout the program
  Understanding customer and business need

## Slide 33: What happens when you click the link?
The browser connects to a Domain Name Server and gets the IP address for the web server
The browser uses an HTTP request to ask the web server for the page
  If the server can’t find the page you get the 404 error
  If the server finds the page, the HTML is returned to your browser and interpreted
The connection is closed
If the page has additional elements such as graphics or video, a new HTTP connection is made for each element on the page.
Remember that each part of the page may be hundreds of packets!